Thank you for choosing ourmechanic lifter. For your safety and correct operation, please carefully read the manual before use.

NOTE: All of the information reported herein is based on data available at the time of printing. The factory reserves the right to modify its own products at any time without notice or incurring in any sanction. Please verify with the factory for possible updates.

1. SPECIFICATION

| Model | MR200 |
| --- | --- |
| Capacity | 200 |
| Platform Height (Max.) (mm) | 120 |
| (Min.) (mm) | 95 |
| Fork width (mm) | 220 |
| Fork length (mm) | 580 |
| Net weight (kg) | 21 |

2. OPERATION

- For moving and transporting display pallets, fruit pallet, etc…

- Large wheels of polyurethane ensuring an excellent manoeuvrability

- Simple to operate

RAISE: Put the No. 10 down, and raised the mechanic lifter, then the operation can trundle the lifter forward location you wanted.

LOWER: Put the No. 10 down while step on the No. 19, and raised the feet slowly until the lifter is lowered the lowest place, then pull the lifter back.

Notice: Please see the below for the No. of part.

3. EXPLODED VIEW & PART LIST

| No. | Description | Qty | Remark |
| --- | --- | --- | --- |
| 1 | Handle | 1 |  |
| 2 | Screw | 6 |  |
| 3 | Clip spring Ф12 | 10 |  |
| 4 | Spring | 1 |  |
| 5 | Pin shaft Ф12×210 | 1 |  |
| 6 | Lift connecter | 1 |  |
| 7 | Nut M16 | 2 |  |
| 8 | Pedal | 1 |  |
| 9 | Wheel Ф120 | 2 |  |
| 10 | Lift pedal | 1 |  |
| 11 | Lift mechanism | 1 |  |
| 12 | Pin shaft Ф12×200 | 1 |  |
| 13 | Pin shaft Ф12×50 | 1 |  |
| 14 | Shaft Ф12×200 | 1 |  |
| 15 | Clip spring | 2 |  |
| 16 | Wheel Ф80 | 2 |  |
| 17 | Pin shaft Ф12×140 | 1 |  |
| 18 | Lift bascule | 1 |  |
| 19 | Pin shaft Ф12×220 | 1 |  |
| 20 | Lift rod | 1 |  |
| 21 | Carriage | 1 |  |

# Text boxes

# Instruction Manual

Mechanic Lifter

Note: The Owner/Operator must read carefully and understand all the information presented here before operation.