FORWARD

Before operating the electric stacker, read this ORIGINAL INSTRUCTION HANDBOOK carefully and understand the usage of the truck completely. Improper operation of the truck may create a danger situation. This handbook describes the usage of different electric stackers. When operating and servicing the truck, make sure, that it applies to your type. 

Keep this handbook for future reference. If this or the warning/caution labels are damaged or got lost, please contact your local dealer for replacement.

This truck complies with the requirements according to EN 3691-1 (Industrial trucks - safety requirements and verification, part 1), EN 12895 (Industrial trucks - electromagnetic compatibility), EN 12053 (Safety of industrial trucks- test methods for measuring noise emissions), EN 1175-1 (Industrial truck safety – electrical requirements), assumed the truck is used according to the described purpose.

The noise level for this machine is < 70 dB(A) according to EN 12053.

ATTENTION:

- Environmentally hazardous waste, such as batteries, oil and electronics, will have a negative effect on the environment or health, if handled incorrectly.

- The waste packages should be sorted and put into solid dustbins according to the materials and be collected disposal by local special environment protection bureau. To avoid pollution, it’s forbidden to throw away the wastes randomly.

- To avoid leaking during the use of the products, the user should prepare some absorbable materials (scraps of wooden or dry duster cloth) to absorb the leaking oil in time. To avoid second pollution to the environment, the used absorbable materials should be handed in to special departments in terms of local authorities.

- Our products are subject to ongoing developments. The information written in this handbook is provided as reference for operating and servicing the stacker and may vary in terms of description of particular features of the truck.

NOTE: On this manual, the left sign means warning and danger, which can lead to death or serious injury if not followed.

Copyright

The copyright remains with the company, mentioned on the CE- certificate at the end of this document or, if sold within the USA, with the company, mentioned on the company sticker.

TABLE OF CONTENTS

1.	CORRECT APPLICATION	3

2.	DESCRIPTION OF THE STACKER	4

a.	Overview of the main components	4

b.	Main technical data	6

c.	Description of the safety devices and warning labels (Europe and others, except USA))	8

d.	Identification plate	9

3.	WARNINGS, RESIDUAL RISK AND SAFETY INSTRUCTIONS	10

4.	COMMISSIONING, TRANSPORTING, DECOMMISSIONING	11

a.	Commissioning	11

b.	Hoisting/ transportation	11

c.	Decommissioning	12

5.	DAILY INSPECTION	12

6.	OPERATION INSTRUCTIONS	13

a.	Parking	13

b.	Residual lift diagram	13

c.	Lifting	14

d.	Lowering	14

e.	Travelling	14

f.	Steering	15

g.	Braking	15

h.	Malfunctions	15

i.	Emergency	15

7.	BATTERY CHARGING AND REPLACEMENT	16

a.	Replacement	16

b.	Battery Indicator	16

c.	Charging	17

8.	REGULAR MAINTENANCE	18

a.	Maintenance checklist	18

b.	Lubricating points	19

c.	Check and refill hydraulic oil	19

d.	Checking electrical fuses	20

e.	Removing, reattaching guarding	20

9.	TROUBLE SHOOTING	21

10.	WIRING/ CIRCUIT DIAGRAM	22

a.	Electrical circuit diagram	22

b.	Hydraulic circuit	24

11.	SPECIALIZED STIPULATIONS FOR THE USA MARKET	25

a.	Foreword/ Compliance	25

b.	Description warning labels (only for USA market)	26

c.	Technical data for US market	28

12.	DECLARATION OF CONFORMITY (valid, if sold within the EU)	30

CORRECT APPLICATION

It is only allowed to use this electric stacker according to this instruction handbook.

The trucks described in this handbook are self-propelled pedestrian controlled electric power stackers, with electrically powered lifting function. The trucks are designed for stacking operations in dedicated racking by lifting and lowering the palletized loads up to the desired lifting heights.

A wrong usage can cause human injuries or can damage equipment.

The operator/ the operating company has to ensure the correct usage and has to ensure, that this truck is used only by staff, which is trained and authorized to use this truck.

The truck has to be used on substantially firm, smooth, prepared, level and adequate surfaces. The truck is intended to be used for indoor applications with ambient temperatures between +5(C and + 40(C and for various transportation applications without crossing permanent obstacles or potholes. The work on ramps is allowed if ramp is not exceeding the allowed angle. While operating, the load must be placed approximately on the longitudinal centre plane of the truck.

Lifting or transporting people is forbidden.

If used on tail lifts or loading ramps, please ensure that these are used correctly according to the operating instructions.

The capacity is marked on capacity sticker as well on the Identification plate. The operator has to consider the warnings and safety instructions.

Operating lighting must be minimum 50 Lux.

Modification

No modifications or alterations to this stacker which may affect, for example, capacity, stability or safety requirements of the truck, shall be made without the prior written approval of the original truck manufacturer, its authorized representative, or a successor thereof. This includes changes affecting, for example braking, steering, visibility and the addition of removable attachments. When the manufacturer or its successor approve a modification or alteration, they shall also make and approve appropriate changes to capacity plate, decals, tags and operation and maintenance handbooks.

Only in the event that the truck manufacturer is no longer in business and there is no successor in the interest to the business, may the user arrange for a modification or alteration to a powered industrial truck, provided, however, that the user:

a) arranges for the modification or alteration to be designed, tested and implemented by an engineer(s) expert in industrial trucks and their safety,

b) maintains a permanent record of the design, test(s) and implementation of the modification or alteration,

c) approves and makes appropriate changes to the capacity plate(s), decals, tags and instruction handbook, and

d) affixes a permanent and readily visible label to the truck stating the manner in which the truck has been modified or altered, together with the date of the modification or alteration and the name and address of the organization that accomplished those tasks.

By not observing these instructions, the warranty becomes void.

DESCRIPTION OF THE STACKER

## Overview of the main parts

- Protective arm

- Platform

- Driving wheel

- Steering wheel

- Charging indicator

- Charging cable

- Emergency button

- Safety (belly) button

- Accelerator

- Multi-function tiller

- Outer covers

- Truck body

- Forks

- Protective mesh or Plexiglas

- Load roller

Hydraulic system

## Main technical data

Fig. 2: Technical data

Table1: Main technical data for standard version

| Type sheet for industrial truck acc. to VDI 2198 |
| --- |
| Distinguishing mark | 1.2 | Manufacturer’s type designation |  | 3600 |
|  | 1.3 | Drive: electric (battery type, mains...), diesel, petrol, fuel gas |  | Battery |
|  | 1.4 | Operator type (hand, pedestrian, standing, order-picker) |  | Pedestrian |
|  | 1.5 | Rated capacity/ rated load | Q(t) | 1.5 |
|  | 1.6 | Load centre distance | C(mm) | 600 |
|  | 1.8 | Load distance, centre of drive axle to fork | X(mm) | 770 |
|  | 1.9 | Wheelbase | Y(mm) | 1232 |
| Weight | 2.1 | Service weight | kg | 865 |
|  | 2.2 | Axle loading, laden front/rear | kg | 830/1535 |
|  | 2.3 | Axle loading, unladen front/rear | kg | 663/202 |
| Tyres, Chassis | 3.1 | Tires: solid rubber, superelastic, pneumatic, polyurethane |  | Polyurethane (PU) |
|  | 3.2 | Tyre size, front | ( x w (mm) | Ф210×70 |
|  | 3.3 | Tyre size, rear | ( x w (mm) | Ф80×70 |
|  | 3.4 | Additional wheels (dimensions) | ( x w (mm) | Ф100×50 |
|  | 3.5 | Wheels, number front/ rear(x=driven wheels) |  | 1x+1/4 |
|  | 3.6 | Thread, front | b10(mm) | 557 |
|  | 3.7 | Tread, rear | b11(mm) | 410/525 |
| Dimensions | 4.2 | Height, mast lowered | h1 (mm) | 2280 |
|  | 4.3 | Free lift | h2 (mm) | 78 |
|  | 4.4 | Lift | h3 (mm) | 3515 |
|  | 4.5 | Height, mast extended | h4 (mm) | 4005 |
|  | 4.9 | Height drawbar in driving position min./max. | h14(mm) | 1100/1360 |
|  | 4.15 | Height, lowered | h13(mm) | 85 |
|  | 4.19 | Overall length | l1(mm) | 1867 |
|  | 4.20 | Length to face of forks | l2(mm) | 717 |
|  | 4.21 | Overall width | b1(mm) | 820 |
|  | 4.22 | Fork dimension | s/ e/ l(mm) | 60/180/1150 |
|  | 4.25 | Fork spread | b5 (mm) | 570/685 |
|  | 4.32 | Ground clearance, centre of wheelbase | m2(mm) | 25 |
|  | 4.33 | Aisle width for pallets 1000X1200 crossways | Ast (mm) | 2330 |
|  | 4.34 | Aisle width for pallets 800×1200 lengthways | Ast (mm) | 2275 |
|  | 4.35 | Turning radius | Wa (mm) | 1487 |
| Performance data | 5.1 | Travel speed, laden/ unladen | km/h | 4.0/4.2 |
|  | 5.2 | Lift speed, laden/ unladen | m/s | 0.068/0.162 |
|  | 5.3 | Lowering speed, laden/ unladen | m/s | 0.142/0.136 |
|  | 5.8 | Max. gradeability, laden/ unladen | % | 5/10 |
|  | 5.10 | Service brake |  | Electromagnetic |
| Electric- motor | 6.1 | Drive motor rating S2 60min | kW | 0.75 |
|  | 6.2 | Lift motor rating at S3 10% | kW | 2.2 |
|  | 6.3 | Battery acc. to DIN 43531/ 35/ 36 A, B, C, no |  | no |
|  | 6.4 | Battery voltage/ nominal capacity K5 | V/Ah | 2x12/106 |
|  | 6.5 | Battery weight | kg | 2x34 |
|  | 6.6 | Energy consumption according to VDI 2198 | kWh/h | 0.70 |
| Additional data | 8.1 | Type of drive unit |  | DC- Speed Control |
|  | 8.4 | Sound pressure at the driver’s seat according to DIN EN 12053 | db(A) | <70 |

| Designation | Lowered mast height h1(mm) | Free Lift height h2(mm) | Lift height h3(mm) | Extended mast height h4(mm) | Lift+fork height h3+h13(mm) |
| --- | --- | --- | --- | --- | --- |
| One stage mast | 1978 | 1510 | 1515 | 1985 | 1600 |
|  | 2378 | 1910 | 1915 | 2385 | 2000 |
| Two stage mast | 1930 | 78 | 2815 | 3305 | 2900 |
|  | 2080 | 78 | 3115 | 3605 | 3200 |
|  | 2280 | 78 | 3515 | 4005 | 3600 |

## Description of the safety devices and warning labels (Europe and others, except USA)

A   Decal (crane hook)

B   Warning decal (do not step under or on the forks)

C   Label (residual lift capacity)

D   Decal (read and follow the instructions)

E   Decal (no passengers)

F   Label (identification plate)

P   Decal (arm pinching)

7   Emergency button

8   Safety (belly) button

10  Multi-function tiller

## Identification plate

- Designation, type

- Serial number

- Rated capacity in kg

- Supply voltage in V

- Own mass (self weight) in kg without battery

- Name and address of manufacturer)

- Battery weight minimum/ maximum

- Nominal power in kW

- Load center distance

- Manufacturing date

Option

WARNINGS, RESIDUAL RISK AND SAFETY INSTRUCTIONS

DO NOT

- Put foot or hand under or into the lifting mechanism.

- Allow other person than the operator to stand in front of or behind the truck when it is moving or lifting/lowering.

- Overload the truck.

- Put foot in front of the wheels, injury could result.

- Lift people. People could fall down and suffer severe injury.

- Push or pull loads; use drawbar

- Side or end load. Load must be distributed evenly on the forks.

- Use the truck with unstable, unbalanced not stable load.

- Use truck without manufacturer’s written consent.

- Lifted loads could become unstable at wind forces. In the case of wind forces do not     lift the load if there is any influence to the stability

- Do not use the truck without help if load is causing insufficient visibility. Operation without help of additional people may result in crushes or injuries. Always make sure the transportation of load is safe.

- Do not operate the truck with removed covers or the apron.

Watch difference in floor levels when driving. Load could fall down or the truck could get uncontrollable. 
Keep watching the condition of load. Stop operating the truck if load becomes unstable.

Brake the truck and activate the emergency button (6) by pushing when sliding load on or off the truck. If the truck has any malfunctions, follow chapter 8. 
Practice maintenance work according to regular inspection. This truck is not designed to be water resistant. Use the truck under dry condition. Prolonged continuous operation might cause damage of the power pack. Stop operation if temperature of hydraulic oil is too high.

- When operating the electric stacker, the operator has to wear safety shoes.

- The truck is intended to be used for indoor applications with ambient temperatures
between +5(C and + 40(C.

- The operating lighting must be minimum 50 Lux.

- To prevent unintended sudden movements when not operating the truck (i.e. from another person, etc.), press emergency switch (6) or press the X button of pin-code panel.

COMMISSIONING, TRANSPORTING, DECOMMISSIONING

Commissioning

Table 2: Commissioning data

| Type | PSE15-C/1600 | PSE15-C/3600 |
| --- | --- | --- |
| Commissioning weight [kg] | 755 | 895 |
| Dimensions [mm] | 1600 | 3600 |

After receiving our new stacker or for re-commissioning you have to do following before (firstly) operating the truck:

- Check if are all parts included and not damaged

- Make sure the tiller is assembled correctly (electrical socket is connected and fixed with two plastic clamps, circlip of the axle is installed)

- Check that battery is charged (follow chapter 8)

- Do the work according to the daily inspections as well as functional checks.

Hoisting/ transportation

For transporting, remove the load, lower the forks to the lowest position and fix the truck safe with dedicated lifting gear according to the following figures.

Hoisting
	USE DEDICATED CRANE AND LIFTING EQUIPMENT

DO NOT STAND UNDER THE SWAYING LOAD

DO NOT WALK INTO THE HAZARDOUS AREA DURING LIFTING

Park the truck securely and lash the truck according to the points identified in Fig. 5. Lift the truck to its destination and place the truck securely before removing the lifting gear. The lashing points are according to the Fig. 5.

Transportation

DURING TRANSPORTATION ON A LORRY OR TRUCK ALWAYS FASTEN THE TRUCK SECURELY

Lower the forks and park the truck securely.

Fasten the truck according to Fig. 6 by fixing dedicated lashing belts to chassis, Fork carriage and mast, and fasten the other side at the transporting truck.

Decommissioning

For storage, remove the load, lower the truck to the lowest position, grease all in this handbook mentioned greasing points (regular inspection), and eventually protect the truck against corrosion and dust. Remove the batteries and jack the truck safely, so that there will be no flattening after storage.
For final decommissioning hand the truck to a designated recycling company. Oil, batteries and electric components must be recycled due to legal regulations.

DAILY INSPECTION

This chapter describes pre-shift checks before putting the truck into operation.

Daily inspection is effective to find the malfunction or fault on this truck. Check the truck on the following points before operation.

Remove load from truck and lower the forks.

DO NOT USE THE TRUCK IF ANY MALFUNCTION IS FOUND.

- Check for scratches, deformation or cracks.

- Check if there is any oil leakage from the cylinder.

- Check the smooth movement of the wheels.

- Check the function of driving in both directions (section 6e).

- Check the functions of braking by activation of tiller arm sensor, reversing of driving buttons, release of driving buttons and of the safety (belly) button (section 6g).

- Check the function of the emergency brake by activating the emergency button.

- Check the lifting and lowering functions by operating the buttons (section 6c and 6d).

- Check the function of steering by turning the tiller from one end position to the other one. The steering should be smooth, without jerks or abnormal sound.

- Check if all bolts and nuts are tightened firmly.

- Visual check if there are any broken electric wires.

- If supplied with a backrest extension, check it for damages and correct assembling.

- Check the presence of warning stickers and signs (section 2c)

If supplied with a backrest extension, check it for damages and correct assembling

OPERATION INSTRUCTIONS

BEFORE OPERATING THIS TRUCK, PLEASE FOLLOW THE WARNINGS AND SAFETY INSTRUCTIONS (CHAPTER 3).

BEFORE OPERATING THIS TRUCK, ENSURE THAT THE LOAD OR OTHER EQUIPMENT NOT CAUSES INSUFFICIENT VISIBILITY!

Ensure that the goods are level and stable, and conduct daily inspections. Press the password numbers manually on the pin code lock (20) and press "√" to start the truck.

Press the horn button (17) to activate the horn.

Parking

DO NOT PARK THE TRUCK ON INCLINED SURFACES

The truck is equipped with an electromagnetic fail-safe stopping and parking brake.

Always lower the forks fully and drive the truck to a safe area. Press the emergency button (7).

Residual lift diagram

The residual lift diagram indicates the maximum capacity Q [kg] for a given load centre c [mm] and the corresponding lift height H [mm] for the truck with horizontal load.
The white markings on the mast indicate if the specific lifting limits reached. For instance with a load centre of gravity distance c of 600 mm and a maximum lift height H of 3600 mm, the max. Capacity Q is 800 kg.

Lifting

DO NOT OVERLOAD THE TRUCK! THE MAXIMUM

CAPACITY IS 1500kg.
LIFT ONLY CAPACITIES ACCORDING TO THE

RESIDUAL LIFT DIAGRAM.

Travel with the lowered forks fully underneath the pallet and press

the lifting button (Fig. 7, 18) until you reached the desired lifting

height.

Lowering

If the forks are in the racking, firstly travel out of the racking carefully with or without the pallet. By travelling out of the racking, take care that the forks are not touching the racking.

Press the lowering button (Fig. 7, 19) carefully.

Lower the load until the forks are clear of the pallet, then drive the truck carefully out of the load unit.

Travelling

TRAVEL ON INCLINES ONLY WITH THE LOAD FACING UPHILL.

DO NOT TRAVEL ON INCLINES MORE THAN SPECIFIED WITH THE TECHNICAL DATA. 
TRAVELLING IS ONLY ALLOWED IF THE FORKS ARE LOWERED DOWN TO THE LIFTING POINT (<300MM).

Carefully pull out the emergency button 7 (Fig. 1) and start the truck by activation from pin-code lock (Fig. 7) access. Then move the tiller to the operating zone (‘F’, Fig.10).
Turn the accelerator knob to the desired direction forward ‘Fw.’ Or backwards ‘Bw.’(Fig. 10).

Control the travelling speed by moving accelerator knob (10) carefully until you reached desired speed.

If you move the accelerator knob back to the neutral position, the controller decelerates the truck until the truck stops. If the truck stops, the parking brake will be engaged.

Carefully drive the truck to the destination. Watch the route conditions and adjust the travelling speed via the accelerator knob.

Steering

Steer the truck by moving the tiller to left or right side.

Braking

PLEASE CHECK THE BRAKING DISTANCE WITH TRUCK BEFORE OPERATION

THE BRAKING PERFORMANCE DEPENDS ON THE TRACK CONDITIONS AND THE LOAD CONDITIONS OF THE TRUCK

The braking function can be activated on several ways:

- By moving the accelerator button (Fig.7, 9) back to the initial ‘0’ position or by releasing the button, the regenerative braking is activated. The truck brakes until it stops.

- By moving the accelerator button (Fig.7, 9) from one driving direction directly to the opposite direction, the truck brakes regenerative until it starts traveling into the opposite direction.

- The truck brakes, if the tiller is moved up or down to the braking zones (‘B’). If the tiller is released, the tiller moves automatically up to the upper baking zone (‘B’).The truck brakes until it stops.

- The safety (belly) button (Fig.7, 8) prevents the operator from being crushed. If this button is activated, the truck decelerates and/ or starts traveling into the backwards direction (‘Bw.’) for a short distance and stops. Please consider, that this button also operates, if the truckis not traveling and the tiller is in the operating zone.

Malfunctions

If there are any malfunctions or the truck cannot be operated, please stop using the truck and activate the emergency button (Fig 1, 7) by pressing it. If possible, park the truck in a safe area.
Inform immediately the manager and, or call your service. If necessary, tow the truck out of the operating area by using dedicated towing/ lifting equipment.

Emergency

In emergencies or in the event of tip over (or off dock), keep safe distance immediately. If possible push the emergency button (Fig 1, 7). All electrical functions will be stopped.

BATTERY CHARGING AND REPLACEMENT

- Only qualified personnel are allowed to service or charge the batteries. The instructions of this handbook and from the battery- manufacturer must be observed.

- The batteries are maintenance free batteries.

- Recycling of batteries undergoes national regulations. Please follow these regulations.

- By handling batteries, open fire is prohibited, gases could cause explosion!

- In the area of battery charging neither burning materials nor burning liquids are allowed. Smoking is prohibited and the area must be ventilated.

- Park the truck securely before starting charging or installing/changing the batteries

- Before finishing the maintenance work, make sure, that all cables are connected correctly and that there are no disturbing towards other components of the truck.

PSE15-C equips with lead-acid battery: 2x12V/ 106Ah, 2x34kg.

IT IS ONLY ALLOWED TO USE LEAD ACID BATTERY FOR ECL15B. IT IS ONLY ALLOWED TO USE LITHIUM BATTERY FOR ECL15N.
PLEASE CONSIDER THE MAXIMUM OPERATING TEMPERATURE OF THE BATTERIES

Replacement

Battery Indicator

- Power display: 10 grids indicate 100% charge, each grid represents 10% charge, every 10% discharge with power out of one grid, if the remaining charge is less than 20%, the grids on the display screen flashes. When the battery is charged to the recovery voltage of the indicator, the display screen will show full recovery charge grids. Every time you turn on the display, the record/ memory is available;

- Hour-meter display: the working time of the truck is recorded in unit (hour) with accuracy of 0.1 hour. Every time you turn on the display, the record/ memory is available;

- Fault code display: it consists of two parts. One is the wrench symbol: wrench symbol showed on the screen indicates the fault of the truck, it will not be on the screen without fault; The other part is fault code: when the wrench symbol is displayed on the screen, the original position of the hour-meter displays the fault code. See the table of fault codes for details (Note: only the fault on the tiller is displayed, the analog signal of the controller is displayed by its own indicator light);

- Turtle speed display: the turtle symbol is normally off. Press the turtle speed button on the tiller, then the turtle symbol will display on the screen and the truck is in slow speed;

- Timing hourglass display: when the hour timing function of the tiller is activated, the hourglass symbol displays on the screen, if not, the hourglass symbol will not display.

Charging

- Before using the charger, please fully understand the instructions of the charger instructions.

- Always follow these instructions.

- The room, where you are charging must be ventilated.

- The exactly charge status can be only checked from the discharge indicator. To control the status, the charging must be interrupted and the truck must be started.

Table 3: LED-Status

| LED- signal | Function |
| --- | --- |
| Red | Battery discharged |
| Orange | Charger or battery failure |
| Green | Fully charged |

REGULAR MAINTENANCE

- Only qualified and trained personnel are allowed to do maintenance on this truck.

- Before maintaining, remove the load and lower the forks to the lowest position.

- If you need to lift the truck, follow chapter 4b by using designated lashing or jacking equipment. Before working, put safety devices (for instance designated lift jacks, wedges or wooden blocks) under the truck to protect against accidental lowering, movement or slipping.

- Please pay attention by maintain the tiller arm. The gas pressure springs are pre-loaded by compression. Carelessness can cause injury.

- Use approved and from your dealer released original spare parts.

- Please consider that oil leakage of hydraulic fluid can cause failures and accidents.

- It is allowed to adjust the pressure valve only from trained service technicians.

Check the items emphasized in maintenance checklist.

Maintenance checklist

Table 4: Maintenance checklist

|  | Interval (Month) |
| --- | --- |
|  | 1 | 3 | 6 | 12 |
|  | Hydraulic |
| 1 | Check the hydraulic cylinder, piston for damage noise and leakage |  | ( |  |  |
| 2 | Check the hydraulic joints and hose for damage and leakage |  | ( |  |  |
| 3 | Inspect the hydraulic oil level, refill if necessary |  | ( |  |  |
| 4 | Refill the hydraulic oil ( 12 month or 1500 working hours) |  |  |  | ( |
| 5 | Check and adjust the function of the pressure valve (1500kg +0/ +10%) |  |  |  | ( |
|  | Mechanical system |
| 6 | Inspect the forks for deformation and cracks |  | ( |  |  |
| 7 | Check the chassis for deformation and cracks |  | ( |  |  |
| 8 | Check if all screws are fixed |  | ( |  |  |
| 9 | Check mast and chain for corrosion, deformation or damages, replace if necessary | ( |  |  |  |
| 10 | Check the gearbox for noise and leakage |  | ( |  |  |
| 11 | Check the wheels for deformation and damages, replace if necessary |  | ( |  |  |
| 12 | Lubricate the steering bearing |  |  |  | ( |
| 13 | Inspect and lubricate the pivot points |  | ( |  |  |
| 14 | Lubricate the grease nipples | ( |  |  |  |
| 15 | Replace the guarding and/or protective screen if it is damaged | ( |  |  |  |
|  | Electric system |
| 16 | Inspect the electric wiring for damage |  | ( |  |  |
| 17 | Check the electric connections and terminals |  | ( |  |  |
| 18 | Test the Emergency switch function |  | ( |  |  |
| 19 | Check the electric drive motor for noise and damages |  | ( |  |  |
| 20 | Test the display |  | ( |  |  |
| 21 | Check if correct fuses are used, if necessary replace. |  | ( |  |  |
| 22 | Test the audio warning signal |  | ( |  |  |
| 23 | Check the contactors |  | ( |  |  |
| 24 | Check the frame leakage (insulation test) |  | ( |  |  |
| 25 | Check function and wear of the accelerator |  | ( |  |  |
| 26 | Check the electrical system of the drive motor |  | ( |  |  |

Lubricating points

Lubricate the marked points according to the maintenance

checklist. The required grease specification is: DIN 51825,

standard grease.

Check and refill hydraulic oil

It is recommended to use hydraulic oil in connection with average temperature:

| Environment temperature | –5℃~25℃ | >25℃ |
| --- | --- | --- |
| Type | HVLP 32, DIN 51524 | HLP 46, DIN 51524 |
| Viscosity | 28.8-35.2 | 41.4 - 47 |
| Amount | 5L (depends on specific model) |

Waste material like oil, used batteries or other must be probably disposed and recycled according to the national regulations and if necessary brought to a recycling company.
The oil level in the oil tank should be between min and max marks with fully lowered forks.
If necessary add oil at the filling point.

Checking electrical fuses

Removing, reattaching guarding

DO NOT USE THIS TRUCK, IF THE GUARDING IS DAMAGED OR NOT CORRECTLY ASSEMBLED!

If the guarding needs to be removed, unscrew carefully. For reattaching place the guarding to its correct position and screw to their original position. If you need to replace parts, please call your service partner. Please make sure that the guarding is fixed correctly and that the fixing elements are not damaged.

TROUBLE SHOOTING

- If the truck has malfunctions follow the instructions, mentioned in chapter 6.

| TROUBLE | CAUSE | REPAIR |
| --- | --- | --- |
| Load can’t be lifted | Load weight too high | Lift only the max. capacity, mentioned on the ID-plate |
|  | Battery discharged | Charge the battery |
|  | Lifting fuse faulty | Check and eventually replace the lifting fuse |
|  | Hydraulic oil level too low | Check and eventually refill hydraulic oil |
|  | Oil leakage | Repair the hoses and/or the sealing of the cylinder |
| Oil leakage from air breathing | Excessive quantity of oil. | Reduce oil quantity. |
| Stacker not starts operating | Battery is charging | Charge the battery completely and then remove the main power plug form the electrical socket. |
|  | Battery not connected | Connect the battery correctly |
|  | The fuse is faulty | Check and eventually replace fuses |
|  | Battery discharged | Charge the battery |
|  | Tiller in the operating zone | Move the tiller firstly to the braking zone. |
| Only travelling in one direction | The accelerator and the connections are damaged. | Check the accelerator and the connections. |
| The stacker only travels very slowly | The battery is discharged. | Check the battery status at the discharge indicator |
|  | The electromagnetic brake is engaged. | Check the electromagnetic brake |
|  | The relating tiller cables are disconnected or damaged | Check the tiller cables and connections. |
| The stacker starts up suddenly | The controller is damaged. | Replace the controller. |
|  | The accelerator not moves back to its neutral position. | Repair or replace the accelerator. |

If the truck has malfunctions and can’t be operated out of the working zone, jack the truck up and go with a load handler under the truck and safe the truck securely. Then move the truck out of the aisle.

WIRING/ CIRCUIT DIAGRAM

Electrical circuit diagram

| Code | Item | Code | Item |
| --- | --- | --- | --- |
| GB | Battery | HA | Horn |
| Et | Controller | FU01 | 80A fuse |
| Mp | Pump motor | FU02 | 200A fuse |
| KMp | Pump contactor | FU1 | 10A fuse |
| SM | Emergency switch | U | 24V charger |
| YV | Electromagnetic valve | XW | Spring cable |
| SU | Micro switch | DT | Detong logic module |
| BE | Accelerator | SH2 | Proximity switch (NC) |
| SA SH SB SJ | Proximity switch (NO) | K K1 | Horn relay |
| Mt | Traction motor | VD | Diode |
| YB | Electromagnetic brake | C | Capacitor |

Hydraulic circuit diagram

Table 8: Description of hydraulic components

| Code | Item | Code | Item |
| --- | --- | --- | --- |
| A | Hydraulic power unit (motor and pump) | E | Throttle valve |
| B | One-way valve | F | Cylinder |
| C | Electromagnetic valve | G | Safety valve |
| D | Relief valve |  |  |

SPECIALIZED STIPULATIONS FOR THE USA MARKET

The content in this chapter is specialized for the US-American market.

- Foreword/ Compliance

Operating this truck requires knowledge which can be acquired from this instruction handbook. This handbook must be kept available throughout the entire period of use of the industrial truck.

IT IS LAW; YOU MUST BE TRAINED AND CERTIFIED TO OPERATE THIS TRUCK! READ AND OBEY ALL WARNINGS AND INSTRUCTIONS IN THIS MANUAL AND ON THE TRUCK!

Only properly trained operators are allowed to operate a powered industrial truck. Your employer must train you and certify, that you are qualified to operate this truck (required by OSHA § 1910.178). The training must satisfy OSHA requirements and as minimum the topics mentioned in this handbook. Depending on the context in this operating manual, the user can refer to several people, including the owner of the truck, anyone who leases or borrows this truck, and the operator as defined in ASME B56.1. Please pay attention to the section in ASME B56.1 concerning the operator. In this standard, it is defined that the safe operation is the responsibility of the operator (ASME B56.1-2003, Part II, section 5.1.1). You and others can be seriously injured or even killed if you don’t use this truck correctly. Before operating your truck, inspect your truck and ensure that it is in correct working order. This truck was designed and built to current industry and government standards. For more information see following: 
- ASME B56.1 (American Society of Mechanical Engineers)
- OSHA §1910.178 (Occupational Safety and Health Act)
- UL 583 (Underwriters Laboratory)
- ANSI Z535.4 (American National Standards Institute)

 This sign indicates hazard situations, if not avoided, will result in serious injury or death. The instructions or precautions to this message must be observed to avoid the potential risk of injury or death.

 If not followed, warning indicates hazard situations which may lead to moderate injury. The instructions or precautions to this message must be observed to avoid the potential risk of injury or death.

 If not followed, caution indicated situations which may lead to minor injury. Instructions or precautions must be observed to avoid minor injury.

- Description of labels and decals (only for USA market)

A  Decal (crane hook)

C  Label (residual lift capacity)

E  Label (identification plate)

F  Decal (read and follow the instructions)

G  Decal (oil filling)

H  Label (no riding)

I   Label (crushing warning)

J   Warning label (warning stay clear stop truck)

L   Label (battery danger)

M   Label (electrical devices)

N   Decal (not under, on forks)

The truck is equipped with an emergency button (6) which stops all lifting-, lowering-, driving- functions and engages the fail-safe electromagnetic brake when it is pushed. The function is described in chapter 2c. Follow the instructions given on the decals. Replace the decals if they are damaged or missing

| Decal (read and follow the instructions) (F) Decal (oil filling) (G) Label (no riding) (H) Label (crushing warning) (I) Label (no adding electrical devices) (M) | Label (be certified and trained) (J) Label (battery danger) (L) Label (no standing/riding on/under forks) (N) |
| --- | --- |

- Technical data for US market

Check page 6 for the drawing.

Table 9: Main technical data for standard version (USA market)

| Type sheet for industrial truck acc. to VDI 2198 |
| --- |
| Distinguishing mark | 1.2 | Manufacturer`s type designation |  | 3600 |
|  | 1.3 | Drive |  | Battery |
|  | 1.4 | Operator type |  | Pedestrian |
|  | 1.5 | Load capacity / rated load | Q (lbs) | 3.3 |
|  | 1.6 | Load center distance | C (in) | 23.6 |
|  | 1.8 | Load distance ,centre of drive axle to fork | X (in) | 30.3 |
|  | 1.9 | Wheelbase | Y(in) | 48.5 |
| Weight | 2.1 | Service weight | lbs | 1907 |
|  | 2.2 | Axle loading, laden front/rear | lbs | 1829.8/3384.1 |
|  | 2.3 | Axle loading, unladen front/ rear | lbs | 1461.7/445.3 |
| Tyres, Chassis | 3.1 | Tires |  | Polyurethane (PU) |
|  | 3.2 | Tire size, front | ( x w (in) | Ф8.3×2.8 |
|  | 3.3 | Tire size, rear | ( x w (in) | Ф3.1×2.8 |
|  | 3.4 | Additional wheels(dimensions) | ( x w (in) | Ф3.9×2 |
|  | 3.5 | Wheels, number front/ rear(x=driven wheels) |  | 1x+1/4 |
|  | 3.6 | Tread, front | b10(in) | 21.9 |
|  | 3.7 | Tread, rear | b11 (in) | 16.1/20.7 |
| Dimensions | 4.2 | Lowered mast height | h1 (in) | 89.8 |
|  | 4.3 | Free Lift height | h2 (in) | 3.1 |
|  | 4.4 | lift | h3 (in) | 138.4 |
|  | 4.5 | Extended maximal height | h4 (in) | 157.7 |
|  | 4.9 | Height of tiller in drive position min./max. | h14(in) | 43.3/53.5 |
|  | 4.15 | Height, lowered | h13(in) | 3.3 |
|  | 4.19 | Overall length | l1(in) | 73.5 |
|  | 4.20 | Length to face of forks | l2(in) | 28.2 |
|  | 4.21 | Overall width | b1(in) | 32.3 |
|  | 4.22 | Fork dimensions | s/ e/ l(in) | 2.4/7.1/45.3 |
|  | 4.25 | Width across forks | b5 (in) | 22.4/27 |
|  | 4.32 | Ground clearance, centre of wheelbase min./max. | m2(in) | 1 |
|  | 4.33 | Aisle width for pallets 1000x1200 crossways | Ast (in) | 91.7 |
|  | 4.34 | Aisle width for pallets 800x1200 lengthwise | Ast (in)) | 89.6 |
|  | 4.35 | Turning radius | Wa (in) | 58.5 |
| Performance data | 5.1 | Travel speed, laden/ unladen | mph | 2.5/2.6 |
|  | 5.2 | Lift speed, laden/ unladen | fpm | 13.4/31.9 |
|  | 5.3 | Lowering speed, laden/ unladen | fpm | 28/26.8 |
|  | 5.8 | Max. gradeability, laden/ unladen | % | 5/10 |
|  | 5.10 | Service brake |  | Electromagnetic |
| Electric- motor | 6.1 | Drive motor rating S2 60min | hp | 1 |
|  | 6.2 | Lift motor rating at S3 10% | hp | 2.95 |
|  | 6.3 | Battery acc. to DIN 43531/ 35/ 36 A, B, C, no |  | no |
|  | 6.4 | Battery voltage, nominal capacity K5 | V/Ah | 2x12/106 |
|  | 6.5 | Battery weight | lbs | 2x75 |
|  | 6.6 | Energy consumption acc. to VDI cycle | kWh/h | 0.7 |
| Addi- tional data | 8.1 | Type of drive control |  | DC- Speed Control |
|  | 8.4 | Sound level at driver`s ear acc. to EN 12053 | db(A) | <70 |

| Designation | Lowered mast height h1(mm) | Free Lift height h2(mm) | Lift height h3(mm) | Extended mast height h4(mm) | Lift+fork height h3+h13(mm) |
| --- | --- | --- | --- | --- | --- |
| one stage mast | 77.9 | 59.4 | 59.6 | 78.1 | 63 |
|  | 93.6 | 75.2 | 75.4 | 93.9 | 78.7 |
| Two stage mast | 76 | 3.1 | 110.8 | 130.1 | 114.2 |
|  | 81.9 | 3.1 | 122.6 | 141.9 | 126 |
|  | 89.8 | 3.1 | 138.4 | 157.7 | 141.7 |

DECLARATION OF CONFORMITY (valid, if sold within the EU)

[GB] CE Declaration of Conformity

The signatory hereby declares that the specified machine conforms to the EU Directive 2006/42/EC (Machine Directive) and 2014/30/EU (Electro-Magnetic Compatibility, EMC) including their amendments as translated into national legislation of the member countries. The signatory is individually authorized to compile the technical documents.

[D] EG-KONFORMITÄTSERKLÄRUNG

Der Unterzeichner bescheinigt hiermit, dass die im Einzelnen bezeichnete Maschine den Europäischen Richtlinien 2006/42/EG (Maschinenrichtlinie) und 2014/30/EU (Elektromagnetische Verträglichkeit - EMV) einschließlich deren Änderungen sowie dem entsprechenden Rechtserlaß zur Umsetzung der Richtlinien in nationales Recht entspricht. Der Unterzeichner ist bevollmächtigt, die technischen Unterlagen zusammenzustellen.

[E] DECLARACIóN DE CONFORMIDAD CE
El signatario certifico por medio de la presente que la máquina especificada cumple con las Normas Europeas 2006/42/CE (Normativa para maquinarias) y 2014/30/EU (Compatibilidad electromagnética), incluyendo sus respectivas odificaciones, así como con el decreto-ley para la adaptación de las normas al derecho nacional. El signatario dispone de una autorización individual que le permitecompilar la documentacióntécnica.

[F] DECLARATION DE CONFORMITE CE

Par la présente déclaration, les soussignés certifient que le machines spécifié ci-dessus est conforme à la loi et aux directives européennes 2006/42/CE (directive sur les machines) et 2014/30/EU (compatibilité électromagnétique - CEM), y compris aux modifications qui y sont apportées et à l’arrêté autorisant sa transposition en droit national. Chaquesignataireesthabilité à établirindividuellement la documentation technique.

[NL] EG-CONFORMITEITSVERKLARING

Ondergetekenden verklaren hierbij dat - volgens de nationale wetgeving van de Lidstaten - de hierboven vermelde opgegeven machina beantwoordt aan de bepalingen qua veiligheid bij machines (EG richtlijn 2006/42/EC) en electro-magnetische compatibilteit (EG richtlijn 2014/30/EU). Ondergetekenden zijn ieder individueel gemachtigd het technisch dossier samen te stellen.

[P] DECLARAÇÃO DE CONFORMIDADE CE
Pela presente, os signatários certificam que o máquina especificado está conforme às Directivas Europeias 2006/42/CE („Máquinas“) e 2014/30/EU („Inocuidade Electromagnética - IEM“), incluindo as alterações das mesmas e o respectivo decreto-lei para a transposição em lei nacional. Cada um dos signatáriosestáautorizado a proceder à elaboração da documentaçãotécnica.

[I] DICHIARAZIONE DI CONFORMITÀ CE
I sottoscrittidichiaranocheilveicolo per trasportiinterniamacchinaspecificatosoddisfa le DirettiveEuropee 2006/42/EC (DirettivaMacchine) e 2014/30/EU (Compatibilitàelettromagnetica - EMV) comprese le relative modifiche, come pure ilrispettivodecretolegislativo per la conversionedelledirettive in dirittonazionale. I sottoscrittisonosingolarmenteautorizzatiallacreazionedelladocumentazionetecnica.

[BG] EВРОПЕЙСКА ОБЩНОСТ - ДЕКЛАРАЦИЯ ЗА СЪОТВЕТСТВИЕ

Подписаните удостоверяват с настоящето, че подробноописанотомашина средствоотговаря на европейския норматив 2006/42/EG (норматив за машини) и на2014/30/EU (електро-магнетична съвместимост), включително с техните промени, както и на съответния указ за прилагане на нормативите в националното право. Подписаните при това са упълномощении поотделно да съставят техническата документация.
[CZ] EG - PROHLÁŠENÍ OSHODĚ

Nížepodepsaný tímtopotvrzuje, žepodrobný popisuvedené strojeodpovídáEvropskýmsměrnicím 2006/42/EC (směrniceprostroje) a 2014/30/EU (elektromagnetická interference - EMV) včetně jejichpozdějších úprav, jakož ipříslušnýmprávnímvýnosůmprouplatnění příslušné směrnicevrámcinárodníhopráva. Každý zpodepsanýchjsoujednotlivě zplnomocněnikvytvoření technickýchpodkladů.
[DK] EF-OVERENSSTEMMELSESERKLÆRING
Undertegnede attesterer hermed, at det specificerede maskine stemmer overens med de Europæiske Direktiver 2006/42/EU (maskindirektiv) og 2014/30/EU (elektromagnetisk kompatibilitet - EMC) samt med den modsvarende lovvedtagelse til implementering af direktiver i den nationale lovgivning. De undertegnede er hver for sig beføjet til at sammenstille de tekniske dokumenter.
[EST] EL vastavusavaldus
Allakirjutanud tõendavad käesolevaga, et üksikasjaliseltkirjeldatudtäpsustatud masin vastab Euroopa direktiividele 2006/42/EÜ (Direktiiv masinate kohta) ja 2014/30/EU (Elektromagnetiline sobivus - EMS) kaasa arvatud nende muudatused ja nendele vastavatele õigusmäärustele direktiivide muutmiseks siseriiklikuks õiguseks. Iga allakirjutanu üksikult on volitatud koostama tehnilist dokumentatsiooni.
[FIN] EU-YHDENMUKAISUUSSELOSTUS
Allekirjoittaneet todistavat täten, että kukin erikseen mainittu omalla voimanlähteellä varustettutehdaskone vastaa EU-direktiivien 2006/42/EC (koneenrakennusdirektiivi) ja 2014/30/EU (sähkömagneettinen yhteensopivuus – EMC) määräyksiä sekä niiden muutoksia ja niiden kansalliseen lainsäädäntöön soveltamista koskevaa oikeussääntöä. Jokaisella allekirjoittaneista on oikeus itsenäisesti laatia

asiaankuuluvia teknisiä asiakirjoja.
[GR] ΔΗΛΩΣΗΣΥΜΜΟΡΦΩΣΗΣΕΟΚ

ΟιυπογράφοντεςβεβαιώνουνδιάτηςπαρούσηςότιτοσυγκεκριμένομηχάνημασυμμορφώνεταιπροςτηνΚοινοτικήΟδηγία 2006/42/ΕΚ («Μηχανήματα») και 2014/30/EU (Ηλεκτρομαγνητικήςσυμβατότητας, Ημσ), καθώςκαιοιτροποποιήσειςτους, όπωςμεταφράστηκεστηνεθνικήνομοθεσίατωνχωρώνμελών. Οιυπογράφοντεςείναισεκάθεπερίπτωσηεξουσιοδοτημένοιατομικάνακαταρτίσουντατεχνικάέγγραφα.

[H] EU KONFORMITÁSI NYILATKOZAT
Alulírottak ezennel igazolják, hogy a részletesen leírt a megadott gép megfelel a 2006/42/EC (Gép-Irányelv) és a 2014/30/EU (Elektromágneses összeférhetőség - EMV) Európai Irányelveknek, beleértve azok módosításait, valamint az irányelvek nemzeti jogba történő átültetésére irányuló megfelelő jogi rendelkezést. Továbbá az alulírottak mindegyike rendelkezik meghatalmazással arra nézve,

hogy összeállíthatja a műszaki dokumentációt.
[LT] ES atitikimơ deklaracija
Žemiau pasirašę asmenys patvirtina,kad atskirai aprašytasnurodyta mašina atitinka Europos Sąjungos direktyvas 2006/42/EB (Mašinų direktyva) ir 2014/30/EU (Elektromagnetinis suderinamumas – EMS) įskaitant jų pakeitimus, o taip pat ir atitinkamą teisės aktą dėl direktyvų įgyvendinimo nacionalinėje teisėje. Kiekvienas iš pasirašiusių asmenų turi teisę ruošti techninę dokumentaciją.

[LV] ES atbilstības deklarācija
Ar zemāk redzamajiem parakstiem tiek apliecināts, kanorādīts mašīna atbilstEiropas Savienības normatīvām 2006/42/EG (Mašīnu normatīvas) un 2014/30/EU (Elektromagnētiskā atbilstība – EMV), ieskaitot to izmaiņas, kā arī atbilstošos tiesiskos rīkojumus normatīvu pielāgošanai

nacionālajai likumdošanai. Parakstu īpašnieki ir atsevišķi pilnvaroti sastādīt tehniskās dokumentācijas.
[N] EU-KONFORMITETSERKLÆRING
Undertegnede bekrefter hermed at de enkelte betegnede maskin med kraftdrift tilsvarer de europeiske retningslinjene 2006/42/EC (maskinretningslinje) og 2014/30/EU (elektromagnetisk fordraglighet - EMV) inklusiv disses endringer og den tilsvarende rettsforordning til omsetning av nasjonal rett. Hver undertegnede er fullmektig til å sette sammen de tekniske dokumentene.

[PL] DEKLARACJA ZGODNOŚCI WE

Niżej podpisani deklarują, że poniżej opisana maszyna spełnia wymagania określone w dyrektywach Europejskich 2006/42/EC (Dyrektywa Maszynowa) i 2014/30/EU (Kompatybilności elektromagnetycznej - EMC) wraz z ich późniejszymi zmianami oraz odpowiednimi rozporządzeniami mającymi na celu przeniesienie tych dyrektyw do prawa krajów członkowskich. Sygnatariusz jest indywidualnieupoważniony do zestawianiadokumentacjitechnicznej.
[RO] DECLARAŢIE DE CONFORMITATE CE
Subsemnaţiiadeverescprinprezentacăvehiculul despecificatmaşinădescris individual corespundedirectiveloreuropene 2006/42/CE (Directivaprivindmaşinile) şi 2014/30/EU (Compatibilitateaelectromagnetică - CEM) inclusivmodificărilorlor precum şiactuluilegislativcorespunzătorprentrutranspunereadirectivelorîndreptnaţional. Subsemnaţii sunt fiecareînparteîmputerniciţisăîntocmeascădocumentaţiatehnică.
[RUS] Декларация соответствия стандартам ЕС
Настоящим лица, подписавшие документ, удостоверяют, что машина с указанной спецификацией соответствует европейским стандартам 2006/42/EG (Транспортная директива) и 2014/30/EU (Электромагнитная совместимость - ЕМС), включая изменения в них, а также соответствующим национальным стандартам и нормам. Каждое по отдельности лицо, подписавшее документ, имеет полномочия для составления технической документации.
[S] EG-KONFORMITETSFÖRKLARING
Undertecknarna intygar härmed att det i detalj betecknade maskin uppfyller de Europeiska direktiven 2006/42/EG (Maskindirektiv) och 2014/30/EU (Elektromagnetisk tålighet - EMV), inklusive ändringarna i detta och den motsvarande rättsförordningen för att omsätta direktiven i nationell rätt. Undertecknarna har var för sig fullmakt att sammanställa den tekniska dokumentationen.
[SK] vyhlásenie o zhode
Dolu podpísaní týmto potvrdzujeme, že podrobný popis uvedené stroje Zodpovedá Európskym smerniciam 2006/42/EC (ernica

pre stroje ) a 2014/30/EU ( elektromagnetická tolerancia – EMV ) vrátane jeho neskorších úprav, rovnako zodpovedá aj príslušným právnym nariadeniam na uplatnenie smerníc v rámci národného práva. Každý z podpísaných je jednotlivo splnomocnený na vytvorenie technických podkladov.
[SLO] EU IZJAVA O SKLADNOSTI
Podpisani s tem potrjujemo, da posamično označeno določeno stroj vozilo odgovarja Evropski direktivi 2006/42/EC (Direktiva o strojih) in 2014/30/EU (Elektromagnetna skladnost - EMV) vključno z njihovimi spremembami ter ustrezno pravno uredbo o prevzemu smernic v nacionalno pravo. Podpisniki so vsakokrat posamezno pooblaščeni za izdajanje tehnične dokumentacije.
[TR] AB Uygunluk Açıklaması
İmza sahibi şahıslar, ayrıntıları belirtilen makine aracının, 2006/42/EC (Makine Yönergesi) ve 2014/30/EU (Elektromanyetik Uyumluluk – EMC) no'lu Avrupa Yönergelerine ve bunların değişiklik sonucu oluşan metinlerine ve yönergelerin milli hukuk hükümlerine dönüştürülmesine dair ilgili hukuk kararnamesine uygun olduğunu tasdik ederler. İmza sahibi şahıslar teknik dosyaları bir araya getirmek için münferiden vekil tayin edildi.

- Type/ Typ/ Tipo/ Modello/ Tyyppi/ Tipo / ΤYΠΟΣ/ Típus/ Tip/ Тип/ Tips/ Tipas/ Tüüp:

- Serial No./ Serien-Nr./ N°. de série/ Serienummer/ Nº de serie/ Numero di serie/ Serienr./ Sarjanro/ αυξάνωναριθμός/ Seriové číslo/ Szériaszám/ Nr.Seryjny/ Serijska številka/ Výrobné číslo/ Серийныйномер/ Seri No./ Seerianr./ Sērijas Nr./ Serijos numeris:

- Year of constr./ Baujahr/ Année de constr./ Bouwjaar/ Año de constr./ Anno di costruzione/ Produktionsår/ Byggeår/ Tillverkningsår/ Valmistusvuosi / Ano de fabrico / έτοςκατασκευής/ Rokvýroby/ Gyártásiév/ Rokprodukcji / Letnik / Годизготовления / Üretimyılı / Väljalaskeaasta / Izgatavošanas gads / Gamybosmetai

- Manufacturer or his authorized representative in Community/ Herstelleroder in der Gemeinschaft ansässigerVertreter/ Fabricant ou son mandataireétabli dans la Communauté/ Fabrikant of zijn in de Gemeenschapgevestigdegemachtigde/ Fabricante o representanteestablecidoen la Comunidad/ ConstrutorouRepresentanteestabelecidonaComunidade/ CostruttoreoppureilsuorappresentantenellaComunità/ Fabrikant ellerdennesiFællesskabetetableredebefuldmægtigede/ Produsenteller agent innenfelleskapet/ Tillverkareeller representant inom EU/ Valmistaja tai yhteisömaassaolevaedustaja / V˘robcenebojehozastoupení/ Gyártó / producent albojegoprzedstawiciel w EG (WspólnotaEuropejska)/ Καηαζθεπαζηήο ή όκηινοηνπηθώλ αληηπξνζώπσλ/ Üreticiya da BölgedekiYetkiliTemsilci/ Proizvajalecalipooblaščenizastopnik s sedežem v EU/ Výrobcaalebozástupca so stálymbydliskom v EÚ / Изготовительилиегопредставитель, зарегистрированный в странеСодружества/ Tootjavõiorganisatsioonispaiknevesindaja/ Ražotājsvaivietējaisuzņēmumapārstāvis / Gamintojasarbašalyjereziduojantisatstovas:

- Date/ Datum/ Data/ Fecha/ datum/ Dato/ päiväys/ Kuupäev/ Datums/дата/ Dátum/ dátum/ tarih/ ημερομηνία

- Authorised signatory/ ImAuftrag/ pour ordre/ Incaricato/ Por orden de/ por procuração/ op last van/ påvegneaf/ påuppdrag/ Etteroppdrag/ psta./ Ülesandel / pavedus / v.i. / Попоручению / megbízásából /длъжностнолице / z pověření / z poverenia / po nalogu / napolecenie / din sarcina / adına / θαη' εληνιή

# Text boxes

Version 08/2020

PSE15-C-SMS-001-EN

xyz

INSTRUCTION MANUAL
		Electric Stacker PSE15-C

WARNING

Do not use the electric truck before reading and understanding these operating instructions.

NOTE:

- Please check the designation of your present type at the last page of this document as well as on the ID-plate.

- Keep for future reference.

Fig. 1: Overview main parts

The truck has an emergency button (6) which stops all lifting-, lowering-, driving- functions and engages the failsafe electromagnetic brake when it is pushed. By pulling this button, the truck can be operated after the controller checked the functions. Before operating, insert the key and turn the switch (2) clockwise. To prevent against unauthorized access, turn the key anti-clockwise and remove it if you do not operate this truck The truck is equipped with a safety (belly) button (7) which switches the driving function away from the operator, if the truck travels towards the operator and the tiller is in its operating zone. Follow also the instructions given on the decals. Replace the decals if they are damaged or missing.

1

2

4

5

3

7

If sold to the EU, here the place of the CE marking

6

8

9

10

11

Fig. 4: Identification plate

Fig. 6: Fixing points

Fig. 5: Lifting with a crane

Fig.7: Tiller operating controls

Fig. 9: Residual lift diagram

Fig.9: Load facing uphill

Fig.10: Operating direction

Park the truck safely, press the emergency button (Fig 1, 7) and turn off the stacker. Remove 7 screws on the main cover (Fig 11, 21), then remove the main cover (Fig 11, 21). Remove the screws on the negative anode from the two batteries (indicated as ‘-’), then remove the screws on the positive anode (indicated as ‘+’), put the wire harness aside, loosen the battery cover and remove it. Observe when removing the battery and do not touch the upper electrical indicator display or the oil tank on the side. Assembling way is in reverse way. Please connect the positive anode of the battery first. Otherwise, the truck will be damaged.

Fig. 12: Battery discharge indicator

Park the truck at a dedicated secured area with a dedicated power supply.

Lower the forks and remove the load;

Switch the truck off, the charger starts charging the battery if the charger plug (Fig.1, 6) is connected to the main power supply.

When charging is finished, disconnect the plug (Fig. 13) from the power supply and place it in the designated area.

Fig. 14: Charging

Fig. 13: LED

- Load roller bearing

- Mast

- Chain

- Steering bearing

- Gear box

- Steering roller bearing

- Tiller steering bearing

Fig. 15: Lubricating points

Table 5: Size of the fuses

|  | Rate |
| --- | --- |
| FU1 | 10A |
| FU 01 | 80A |
| FU 02 | 200A |

Fig. 16: Location of fuses

Table 6: Trouble shooting

Fig. 17: Electrical diagram (PSE15-C)

Table 7: Description of electrical components

Fig. 18: Hydraulic circuit diagram

Fig. 19: Warning labels and safety devices (only USA market)

CE-DD-002

- Type:			XX XX–Self propelled industrial truck

- Serial No: 		XXXXXXXX

- Year of constr.:	YYYY

- Manufacturer or his authorized representative in Community:
				Company name/ Street / Postal code Town/ Country

- Date:			YYYY.MM.DD

- Authorized signatory:	Mr. Sample