### Operating instructions

Parts List

## EMS Electric Stacker

Note: Operator MUST read and understand this operating instructions before use this Electric Stacker

Thanks for using our EMS series of Semi-Electric Stacker.Your Electric Stacker is made by special profiles.It is designed compactly and durably. It is easy to handle.For your safety and correct operation,please read this instructions carefully before using.

NOTE: All of the information reported herein is based on data available at the moment of printing. The factory reserves the right to modify its own products at any moment without notice and incurring in any sanction. So, it is suggested to always verify possible updates.

- structural data form

| model |  | EMS10 | EMS15 | EMS20 |
| --- | --- | --- | --- | --- |
| Capacity | Kg | 1000 | 1500 | 2000 |
| Max.Height | mm | 800/1600/2000/2500/3000 | 1600/2000 |
| Fork Size | mm | 570X1000（1100/1150） | 570X1000 |
|  |  | （330—680）×1000（1100/1150） | （330—680）×1000 |
| Single Fork Size | mm | 150X1000（1500） | 150X1000（1500） |
| Overall min.Height | mm | 1000/1980/1780/2030/2380 | 1980/1780 |
| Fork Min.Height | mm | 85 | 85 | 85 |
| Lifting speed | Empty | mm/s | 130 | 130 |
|  | Full |  | 80 | 70 |
| Decline speed | Empty |  | 0~190 | 0~200 |
|  | Full |  | 0~400 | 0~300 |
| Battery |  | DC12V 120Ah | DC12 150Ah |
| Pump Motor |  | DC12V 1.6Kw | DC12V 1.6Kw |

- safety guidance

2.1 Operators should read all warning sings and instructions here and on the Electric Stacker before using it.

2.2 Please don’t use this Electric Stacker before training or authorizing.

2.3 Please check up this Electric Stacker carefully before operating. Especially the wheels, the handles, the rollers, the masts, the battery . ect.

2.4 Please don’t use it on a slopping ground.

2.5 please don’t take up any people on the forks.

2.6 Please don’t touch the masts when lifting the goods.

2.7 The operator had better take on gloves and non-slip shoes for labor protecting.

2.8 Please don’t make the forks over 300mm height when transporting goods.

2.9 All non-essential personnel should leave the stacker more than 600mm when lifting or transporting goods. People forbid standing under the forks.

2.10 Cargo weight should be distributed as evenly as possible on the two forks, do not use only one fork. The center of gravity of goods should be in the center of two forks.

2.11 Please don’t load over maximum capacity.

2.12 Please check up the Battery fluid before using or charging. Add distilled water when it is insufficient.

2.13 The surrounding environment should be dry, well-ventilated and away from flames while charging.

2.14 The fork should be reduced to the lowest point when not using.

2.15 At other special condition or place, the operator should be more carefully to operate the electric stacker.

3 Maintenance

3.1 Hydraulic oil

Please check the oil level every six mouths. The oil can be hydraulic oil:ISO VG32，its viscosity should be 32cSt at 40℃，total volume is about 2.0lt.

3.2 Daily check and maintenance

In order to keep good using status,the operator should make the necessary check and maintain  for the electric stacker daily. At this point the focus should be checked: (1)wheels and mandrel, such as wound on wheels, mandrels’ lines，rags and other objects;(2) the forks and mast are deformation or not;(3) the voltage of battery is normal or not. Please unload the goods and decline the forks to the lowest position when used up.

3.3 Lubrication

Operator should often put butter or lubrication into all movable parts.

4. Battery charging

4.1 Please charge when the battery voltage is lower than 10V.

4.2 Please check up the Battery fluid before charging. Adding distilled water when it is insufficient.

4.3 The surrounding environment should be dry, well-ventilated and away from flames while charging.

4.4 Please charge once a week if unused for a long time and every time shouldn’t be shorter than 2 hours.

4.5 The voltage by instruction sheet shows should lower than 16V.

4.6 Prohibited using when charging.

5.Control Platform

1 Emergency switch  2 coulomb meter 3 charging indicator 4 key switch 5 Button 6 charging plug

5.1 Emergency switch

The Pump motor power supply will be powered off when press the button down; The motor power will be powered on when you turn it clockwise.

5.2 coulomb meter

This meter will show the voltage of battery.If it shows lower than 10V the electric stacker should be charged.

5.3 charging indicator

During the charging process, the indicator light will change color according to the battery level

5.4 key switch

5.5 Button

Control lifting or lowering

6.Trouble Shooting

| No. | Trouble | Clause | Fixing Methods |
| --- | --- | --- | --- |
| 1 | The forks can not be up the Max. height. | —The hydraulic oil is not enough. | —Pour in the hydraulic oil. |
| 2 | The forks can not be lifted up. | —Without hydraulic oil. —The hydraulic oil has impurities. | —Fill in the hydraulic oil. —Change the htdraulic oil. |
| 3 | The pump can’t turn. | —Without put on the emergency switch. —The battery voltage is too low. —The power cord connector is loose. —The motor contactor is broken. | —Turn the emergency switch clockwise. —Charge it. —Screw it. —Replace with the new one. |
| 4 | The forks can not be descended. | —The piston rod or pump body is deformed resulting from piston rod or partial loading slanting to one side or over-loading. —The fork was kept in the high position for long time with piston rod bared to arise in rusting and jamming of the rod. —Hydraulic pump station release valve due to wear or damage, can not be opened. | —Replace the piston rod or pump body. —Keeping the fork in the lowest position if not using, and pay more attention to lubricate the rod. —Change the pump release valve. |
| 5 | Oil spill | —Seals aging or damaged —some parts is broken | —Change new one. —Change new one. |
| 6 | The fork descends without the release valve worked. | —The impurities in the oil cause the release valve to be unable to close tight. —Some parts of hydraulic system is cracked or bored. —The relief value is broken. | —Change the hydraulic oil. —Change new one —Change new one |
| 7 | The battery can’t charge. | —The Battery is broken. —Charging plug is loose. | —Change new one —Interpolate tightly |

NOTE: DO NOT ATTEMP TO REPAOR THE ELECTRIC STACKER UNLESS YOU ARE TRAINED AND AUTHORIZED TO DO SO.

| No. | Name | Quantity | No. | Name | Quantity | No. | Name | Quantity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Top beam seat | 1 | 40 | Screw | 6 | 79 | Bearing | 4 |
| 2 | Bolt | 1 | 41 | Pin | 2 | 80 | Rear wheel | 2 |
| 3 | Top beam axis | 1 | 42 | Guide frame | 2 | 81 | Right wheel frame | 1 |
| 4 | Hole Collar | 2 | 43 | Roller | 2 | 82 | Sprocket wheel | 2 |
| 5 | Bearing | 2 | 44 | Frame | 1 | 83 | Pin | 1 |
| 6 | Sprocket wheel | 2 | 45 | Fixing ring | 1 | 84 | Bearing | 1 |
| 7 | Shaft Collar | 2 | 46 | Nut | 3 | 85 | Bearing | 1 |
| 8 | Screw | 1 | 47 | Screw | 1 | 86 | Dust cap | 1 |
| 9 | Lifting mast | 1 | 48 | Nut | 2 | 87 | Screw | 1 |
| 10 | Chain | 04A | 49 | Fence | 1 |  |  |  |
| 11 | Links head | 2 | 50 | Washer | 4 |  |  |  |
| 12 | Pin | 2 | 51 | Washer | 4 | 90 | Chain | 1 |
| 13 | Bolt | 2 | 52 | Screw | 4 | 91 | Handle Block | 1 |
| 14 | Nut | 2 | 53 | Gauntlets Components | 2 | 92 | Pin | 1 |
| 15 | Nut | 2 | 54 | Charge Indicator | 1 | 93 | Screw | 1 |
| 16 | Fixed width fork tripod | 1 | 55 | Emergency switch | 1 | 94 | Screw | 2 |
| 17 | Shaft circlip | 4 | 56 | Cover |  | 95 | Battery fixing ring | 1 |
| 18 | Guide wheel | 4 | 57 | Under cover | 1 | 96 | Battery | 1 |
| 19 | Bearing | 4 | 58 | Screw | 2 | 97 | Jacket | 1 |
| 20 | Hole circlip | 4 | 59 | Dust cap | 2 | 98 | Screw | 4 |
| 21 | Shaft circlip | 4 | 60 | Bearing | 2 | 99 | coulomb meter | 1 |
| 22 | Guide wheel | 4 | 61 | Bearing | 2 | 100 | Key lock | 1 |
| 23 | Bearing | 4 | 62 | Left wheel frame | 1 | 101 | Hydraulic power unit | 1 |
| 24 | Hole circlip | 4 | 63 | Handle assembly | 1 | 102 | Charger | 1 |
| 25 | Rocker | 4 | 64 | Gas spring | 1 |  |  |  |
| 26 | Axis | 4 | 65 | Axis | 1 | 104 | Shaft Collar | 2 |
| 27 | Spacer | 8 | 66 | Screw | 1 | 105 | Stop collar | 1 |
| 28 | Bearing | 8 | 67 | Bushings | 2 | 106 | The hydraulic cylinder | 1 |
| 29 | Front wheel | 4 | 68 | Pin | 1 | 107 | Tubing connector | 1 |
| 30 | Screw | 2 | 69 | Pedal | 1 | 108 | Tubing | 1 |
| 31 | Lower support plate | 1 | 70 | Shaft Collar | 1 | 109 | Tubing connector | 1 |
| 32 | Nut | 2 | 71 | Axis | 1 | 110 | Gasket | 2 |
| 33 | Seals | 1 | 72 | Brake Pads | 1 | 111 | Spring pin | 8 |
| 34 | Oriented band | 1 | 73 | Screw | 1 | 112 | Shaft circlip | 2 |
| 35 | O-Seals | 2 | 74 | Spring | 1 | 113 | Axis | 1 |
| 36 | Piston | 1 | 75 | Screw | 2 | 114 | Prong | 2 |
| 37 | Rod | 1 | 76 | Nut | 2 | 115 | Guide plate frame | 1 |
| 38 | Nut | 1 | 77 | Spacer | 4 | 116 | Button | 2 |
| 39 | Dust ring | 1 | 78 | Bushings | 2 |  |  |  |