| Instruction Manual Electric Platform (Fork) Stacker Model: EPA EFA EJA |
| --- |
| EPA. Series Stacker | EFA (EJA). Series Stacker |
| NOTE: Owner and Operator must read and understand this instruction manual before using the Electric Stacker. |

CONTENTS

- Brief Introduction………………………………....…………… 2

- Specification…………………………………………………… 2

- Nomenclature Of Each Section………………………………5

- Safety Instruction…………………..…………………………. 5

- Inspection Before Use……………………………………….. 5

- Operation Instruction……………………….…………………6

- Daily Maintenance & Periodical Inspection………………... 6

- Problems & Solution………………………………................ 7

- Diagram of Hydraulic System……………………………….. 8

- Diagram of Electric Control System……………………….. 8

- Exploded View & Parts List……………………………….... 9

Thank you very much for selecting our ELECTRIC STACKER!

This instruction manual describes correct operating method to ensure prolonged service life. Please read and completely understand this manual before operating the Electric Fork Stacker. Always keep this manual at an appropriate place. If the manual or warning decal is missing, please contact your vender.

NOTE:  All information reported herein is based on the data available at the time of printing. The factory reserves the right to modify its own products at any time without notice or incurring in any sanction. Please verify with the supplier for possible updates.

- Brief Instruction

EPA. EFA. EJA series Stacker is designed on the basis of Manual series Stacker. With a power pack and a high quality free-service battery, it is able to lifting or lowering load when operate. It can release labor and improve working efficiency. It mainly applies to transporting, lifting and stacking goods on level place. It is applicable widely in factory, store, hospital, warehouse etc. It becomes a most popular transporter with its many features such as easily operated, safety, automatic, high working efficiency. Low profile forks can lift the pallet easily. Meanwhile place the optional attachment (platform) on the fork, it will be used as a platform stacker.

- Specification

(1) EPA Series Stacker

| Model | EP2120A | EP4120A | EP4150A |
| --- | --- | --- | --- |
| Capacity (Kg) | 200 | 400 | 400 |
| Min. Platform Height H1(mm) | 200 | 200 | 200 |
| Max.Platform Height H2(mm) | 1200 | 1200 | 1500 |
| Platform Length L1(mm) | 600 | 650 | 650 |
| Platform Width W (mm) | 500 | 550 | 550 |
| Dia of Front Wheel d (mm) | Ф125 | Ф150 | Ф150 |
| Dia of Steering Wheel D(mm) | Ф125 | Ф150 | Ф150 |
| Power Pack Motor (KW) | 0.8 | 0.8 | 0.8 |
| Battery (v/Ah) | 12/60 | 12/70 | 12/70 |
| Overall Length L(mm) | 1020 | 1100 | 1100 |
| Overall Width B(mm) | 540 | 580 | 580 |
| Overall Height H(mm) | 1320 | 1320 | 1620 |
| Net Weight (Kg) | 93 | 113 | 118 |

(2) EFA Series Stacker

| Model | EF2120A | EF4120A | EF4150A |
| --- | --- | --- | --- |
| Capacity (Kg) | 200 | 400 | 400 |
| Min. Fork Height H1(mm) | 85 | 85 | 85 |
| Max. Fork Height H2(mm) | 1200 | 1200 | 1500 |
| Fork Length L1(mm) | 600 | 650 | 650 |
| Fork Width W (mm) | 500 | 550 | 550 |
| Single Fork Width W1(mm) | 100 | 100 | 100 |
| Dia of Front Wheel d (mm) | Ф75 | Ф75 | Ф75 |
| Dia of Steering Wheel D(mm) | Ф125 | Ф125 | Ф125 |
| Chassis Height h(mm) | 32.5 | 22.5 | 22.5 |
| Power Pack Motor (KW) | 0.8 | 0.8 | 0.8 |
| Battery (v/Ah) | 12/60 | 12/70 | 12/70 |
| Overall Length L(mm) | 1040 | 1120 | 1120 |
| Overall Width B(mm) | 540 | 580 | 580 |
| Overall Height H(mm) | 1430 | 1430 | 1730 |
| Option Platform (mm) | LP10(610×530) | LP20(660×580) |
| Net Weight (Kg) | 97 | 117 | 122 |

(3) EJA Series Stacker

| Model | EJ2120A | EJ4120A | EJ4150A |
| --- | --- | --- | --- |
| Capacity (Kg) | 200 | 400 | 400 |
| Min. Fork Height H1(mm) | 85 | 85 | 85 |
| Max. Fork Height H2(mm) | 1200 | 1200 | 1500 |
| Fork Length L1(mm) | 600 | 650 | 650 |
| Fork Width W (mm) | 500 | 550 | 550 |
| Single Fork Width W1(mm) | 100 | 100 | 100 |
| Dia of Front Wheel d (mm) | Ф75 | Ф75 | Ф75 |
| Dia of Steering Wheel D(mm) | Ф125 | Ф125 | Ф125 |
| Power Pack Motor (KW) | 0.8 | 0.8 | 0.8 |
| Battery (v/Ah) | 12/60 | 12/70 | 12/70 |
| Overall Length L(mm) | 1080 | 1160 | 1160 |
| Overall Width B(mm) | 540 | 580 | 580 |
| Overall Height H(mm) | 1430 | 1430 | 1730 |
| Option Platform (mm) | LP10(610×530) | LP20(660×580) |
| Net Weight (Kg) | 100 | 121 | 126 |

(4) Loading Capacity Chart:

- Nomenclature of Each Section

1 —— Front Wheel                        6 —— Chain Wheel

2 —— Chassis                            7 —— Handle Rack

3 —— Fork Assembly (Drawer)              8 —— Electric Control Box

4 —— Optional Platform                    9 —— Power Cable for Charging

5 —— Pump Assembly                    10 —— Steering Wheel

4. Safety Instruction

4.1 Use it on a level paved surface.

4.2 Don’t load over the maximum capacity and ensure the balance of loading.

4.3 To cooling the temperature of power pack motor, it should be paused working for minutes after continuous working with load. Otherwise, it might cause damage to power pack.

4.4 Recharge the battery when it has no enough power. Ensure local electric power matches the charge. Do not discharge the battery completely.

4.5 Don’t touch the chain or any other moving parts.

4.6 Please close the electric control box before use.

5. Inspection before Use

As EPA. EFA. EJA series Stacker is integer packing, it was adjusted. The owner should inspect the stacker before use as follows:

5.1 Ensure all parts complete and in good condition. Do not use the stacker and contact local supplier in case of any parts missing or defective.

5.2 Check electric control box.

5.3 Ensure oil is full and no oil leakage in the hydraulic system.

5.4 Ensure battery has enough power. The battery has been charged before shipment.

But due to long time delivery, it would be low in power. When turn on the stacker, the

Voltage meter shows 10.5V, or when lifting loaded, the coulometer shows 3 graduation and green lights, it needs recharged.

5.5 Connect the power, the performance of lifting and lowering platform (fork) is normal when unloaded.

5.6 Connecting power, when loaded platform (fork) lift and lower, there is no oil leak.

5.7 Place the charger at a safety place.

6. Operation Instruction

6.1 Lift/lowering the platform (fork)

6.1.1 Lock the parking brake.

6.1.2 Turn the switch to ON, there is power and all graduation of coulometer is light or voltage meter shows over 10.5V.

6.1.3 Press the LIFT button, the platform (fork) will lift up. Loose the button, the platform (fork) will stop at any position as you like. It will not slide down.

6.1.4 Press the LOWER button, the platform (fork) will lower down. Loose the button, the platform (fork) will stop at any position as you like. It will not slide down.

6.1.5 To prolong the service life of electric pump, it is necessary to loose the button when the platform (fork) reach the top position.

6.1.6 The electric pump is provided with a relief valve. When the load is over 120% of the capacity, the platform (fork) will not lift.

6.1.7 Do not keep the stacker work with load continuously to prevent the motor burned.

6.1.8 When moving the stacker, the clearance between the platform (fork) and ground should be more then 200mm.

6.1.9 In order to keep the stability of stacker should move slowly and the distance is short to the full when stacking the load.

6.1.10 To ensure the safety, turn the switch to OFF and take away the switch key after operation.

6.2 How to use charger

6.2.1 After continuous working, the battery will be low in power. The coulometer is becoming green (3 graduation) or voltage meter shows 10.4V, it will be recharged.

6.2.2 The red light ＜3 graduation on coulometer is showing or voltage meter shows under 10.4V, and lifting speed slow down obviously, it must be recharged. If not, it will shorten the service life of electric pump and battery.

6.2.3 Before recharging the battery, please carefully read and fully understand the attached instruction manual of charger.

6.2.4 Before plugging the charger into a power socket. Make sure local electric power matches the charger. Then connect the charger to socket in the electric control box, the battery will be recharged automatically.

6.2.5 When charging, there will separate out hydrogen and oxygen. So please keep ventilated and away from the fire in case of danger.

7. Daily Maintenance & Periodical Inspection

7.1 Inspect the each section for loose bolts and nuts monthly.

7.2 Inspect the each section, wheel, hydraulic system, electric pump for distortion, worn, and abnormal noise monthly.

7.3 Inspect performance of lifting and lowering the fork and other device monthly.

7.4 Inspect the battery surface for clean and dry monthly. Dirty and wetness may cause leakage of electricity and descent of voltage.

7.5 Inspect the terminals, inserters, fuse electric component for loose, broken monthly.

7.6 Change the hydraulic oil after 20 working hours in the beginning. Then, change the oil every 300 working hours. If the stacker is not used frequently, please change the oil every 18 months.

7.7 Refer to following sheet when change or fill the oil.

| Temperature | Oil |
| --- | --- |
| -5°C～+45°C | L-HM68 Hydraulic oil (equivalent to ISO VG68) |
| -15°C~-5°C | L-HM46 Hydraulic oil (equivalent to ISO VG46) |

7.8 When changing the oil, put the piston at the lowest position, then open the electric control box, remove the bolt on the bottom the valve plate and the bolt connecting motor and valve plate, the pump section is disassembled.

7.9 Clean the valve plate and the oil tank, then fill oil to 80% of oil tank content. And inspect the connection to avoid oil leakage.

7.10 Assemble the section and ensure all parts fastness.

8. Trouble Shooting & Maintenance

| No. | Problem Description | Cause | Remedy |
| --- | --- | --- | --- |
| 1 | Turn the key switch to ON, coulometer doesn’t indicate. | 1.Switch is out of order. 2.Terminals and inserters are loose. | 1.Check and change switch. 2.Check terminals and inserters. |
| 2 | Platform(Fork) does not lift up when pushing LIFT button | 1.Switch is out of order. 2.Fuse is broken. 3.Terminals and inserters are loose. 4.Electric pump is empty of oil. | 1.Check and change switch. 2.Replace fuse. 3.Check terminals and inserters. 4.Fill oil to prescribe position. |
| 3. | Lifting speed is too slow when pushing LIFT button. | 1.Battery is not enough power. 2.Relief valve is not in proper position. | 1.Recharge the battery. 2.Adjust the relief valve. |
| 4. | Fork can’t lift to top. | Electric pump is short of oil. | Fill oil to prescribe position. |
| 5. | Electric pump does not work. | 1.Electric pump is broken. 2.Terminals and connector are loose. 3.Battery is not enough power. | 1.Check and change. 2.Check terminals and inserters. 3. Recharge the battery. |
| 6. | Platform(Fork) does not lower down when pushing LOWER button | 1. Switch is out of order. 2. Fuse is broken. 3.Magnet contactor is broken. 4.Other object block.. | 1.Check and change switch. 2. Replace fuse. 3. Check and change. 4.Remove the object. |

| 7. | Coulometer shows nothing, or the red light flash, or battery has no enough power | 1.Terminals and inserters are loose. 2.Charging time is not enough. 3.Battery is out of order. | 1.Check terminals and inserters. 2. Charge longer time. 3.Check and replace the battery. |
| --- | --- | --- | --- |
| 8 | Hydraulic system has oil leakage. | Oil seals are broken. | Replace oil seals. |
| 9 | After recharging, the coulometer shows low electricity, and lifting speed is slow. | 1.Battery has not enough recharging. 2. Battery is worn out. 3.Charger is worn out. | 1.Recharge the battery. 2.Replace the battery. 3.check and replace the charger. |

9. Diagram of Hydraulic System

10. Diagram of Electric Control System

11.  Exploded View & Parts List

11.1 Exploded View of EPA Series Stacker

11.2 Parts List of EPA Series Stacker

| No. | Description | Qty | Remark | No. | Description | Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Handle rack | 1 |  | 26 | Chain | 1 |  |
| 2 | Nut | 2 |  | 27 | Bearing | 1 |  |
| 3 | Washer | 2 |  | 28 | Chain roller | 1 |  |
| 4 | Screw | 2 |  | 29 | Chain roller cover | 1 |  |
| 5 | Bolt | 4 |  | 30 | Pin | 1 |  |
| 6 | Nut | 4 |  | 31 | Blot | 2 |  |
| 7 | Retaining ring | 4 |  | 32 | Screw | 1 |  |
| 8 | Bolt | 4 |  | 33 | Dustproof ring | 1 | Easy-worn |
| 9 | Washer | 4 |  | 34 | Upper cover | 1 |  |
| 10 | Roller | 4 |  | 35 | Location ring | 1 |  |
| 11 | Bearing | 4 |  | 36 | Piston rod | 1 |  |
| 12 | Pin for roller | 4 |  | 37 | Piston | 1 |  |
| 13 | Platform | 1 |  | 38 | O ring | 1 | Easy-worn |
| 14 | Drawer | 1 |  | 39 | O ring | 1 | Easy-worn |
| 15 | Front Wheel | 2 |  | 40 | Y Sealing ring | 1 | Easy-worn |
| 16 | Bearing | 4 |  | 41 | Retaining ring | 1 |  |
| 17 | Retaining Ring | 4 |  | 42 | Washer | 1 |  |
| 18 | Retaining Ring | 4 |  | 43 | Screw | 1 |  |
| 19 | Pin for Front Wheel | 2 |  | 44 | Location plate | 1 |  |
| 20 | Chassis | 1 |  | 45 | Cylinder | 1 |  |
| 21 | Nut | 2 |  | 46 | Base for oil cylinder | 1 |  |
| 22 | Lock washer | 2 |  | 47 | Union | 2 |  |
| 23 | Steering wheel | 2 |  | 48 | Oil tube | 1 |  |
| 24 | Pin | 2 |  | 49 | Base for electric box | 1 |  |
| 25 | Bolt for chain | 2 |  | 50 | Electric control box | 1 |  |

11.3 Exploded View of EFA Series Stacker

11.4 Parts List of EFA Series Stacker

| No. | Description | Qty | Remark | No. | Description | Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 101 | Handle rack | 1 |  | 126 | Chain | 1 |  |
| 102 | Nut | 2 |  | 127 | Bearing | 1 |  |
| 103 | Washer | 2 |  | 128 | Chain roller | 1 |  |
| 104 | Screw | 2 |  | 129 | Chain roller cover | 1 |  |
| 105 | Bolt | 4 |  | 130 | Pin | 1 |  |
| 106 | Nut | 4 |  | 131 | Blot | 1 |  |
| 107 | Retaining ring | 4 |  | 132 | Screw | 1 |  |
| 108 | Bolt | 4 |  | 133 | Dustproof ring | 1 | Easy-worn |
| 109 | Washer | 4 |  | 134 | Upper cover | 1 |  |
| 110 | Roller | 4 |  | 135 | Location ring | 1 |  |
| 111 | Bearing | 4 |  | 136 | Piston rod | 1 |  |
| 112 | Pin for roller | 4 |  | 137 | Piston | 1 |  |
| 113 | Fork | 1 |  | 138 | O ring | 1 | Easy-worn |
| 114 | Platform | 1 |  | 139 | O ring | 1 | Easy-worn |
| 115 | Pin for front wheel | 2 |  | 140 | Y Sealing ring | 1 | Easy-worn |
| 116 | Retaining ring | 4 |  | 141 | Retaining ring | 1 |  |
| 117 | Retaining ring | 4 |  | 142 | Washer | 1 |  |
| 118 | Bearing | 4 |  | 143 | Screw | 1 |  |
| 119 | Front wheel | 2 |  | 144 | Location plate | 1 |  |
| 120 | Chassis | 1 |  | 145 | Cylinder | 1 |  |
| 121 | Nut | 2 |  | 146 | Base for oil cylinder | 1 |  |
| 122 | Lock washer | 2 |  | 147 | Union | 2 |  |
| 123 | Steering wheel | 2 |  | 148 | Oil tube | 1 |  |
| 124 | Pin | 2 |  | 149 | Base for electric box | 1 |  |
| 125 | Bolt for chain | 2 |  | 150 | Electric control box | 1 |  |

  - Exploded View of EJA Series Stacker

  - Parts List of EJA Series Stacker

| No. | Description | Qty | Remark | No. | Description | Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 201 | Handle rack | 1 |  | 228 | Pin | 2 |  |
| 202 | Nut | 2 |  | 229 | Bolt for chain | 2 |  |
| 203 | Washer | 2 |  | 230 | Chain | 1 |  |
| 204 | Screw | 2 |  | 231 | Bearing | 1 |  |
| 205 | Bolt | 4 |  | 232 | Chain roller | 1 |  |
| 206 | Nut | 4 |  | 233 | Chain roller cover | 1 |  |
| 207 | Retaining ring | 4 |  | 234 | Pin | 1 |  |
| 208 | Bolt | 4 |  | 235 | Blot | 1 |  |
| 209 | Washer | 4 |  | 236 | Screw | 1 |  |
| 210 | Roller | 4 |  | 237 | Dustproof ring | 1 | Easy-worn |
| 211 | Bearing | 4 |  | 238 | Upper cover | 1 |  |
| 212 | Pin for roller | 4 |  | 239 | Location ring | 1 |  |
| 213 | Shelf | 1 |  | 240 | Piston rod | 1 |  |
| 214 | Retaining ring | 2 |  | 241 | Piston | 1 |  |
| 215 | Long Shaft | 1 |  | 242 | O ring | 1 | Easy-worn |
| 216 | Bushing | 2 |  | 243 | O ring | 1 | Easy-worn |
| 217 | Fork | 2 |  | 244 | Y Sealing ring | 1 | Easy-worn |
| 218 | Platform | 1 |  | 245 | Retaining ring | 1 |  |
| 219 | Front Wheel | 2 |  | 246 | Washer | 1 |  |
| 220 | Bearing | 4 |  | 247 | Screw | 1 |  |
| 221 | Retaining ring | 4 |  | 248 | Location plate | 1 |  |
| 222 | Retaining ring | 4 |  | 249 | Cylinder | 1 |  |
| 223 | Pin for front wheel | 2 |  | 250 | Base for oil cylinder | 1 |  |
| 224 | Chassis | 1 |  | 251 | Union | 2 |  |
| 225 | Nut | 2 |  | 252 | Oil tube | 1 |  |
| 226 | Lock washer | 2 |  | 253 | Base for electric box | 1 |  |
| 227 | Steering wheel | 2 |  | 254 | Electric control box | 1 |  |

  - Exploded View of Electric Control Box

  - Parts List of Electric Control Box

| No. | Description | Qty | Remark | No. | Description | Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Battery | 1 |  | 10 | Switch | 1 |  |
| 2 | Connector | 2 |  | 11 | Coulometer | 1 |  |
| 3 | Nut | 2 |  | 12 | Operation handle | 1 |  |
| 4 | Case | 1 |  | 13 | Charging Status | 1 |  |
| 5 | Charger | 1 |  | 14 | Faceplate | 1 |  |
| 6 | Electric Pump | 1 |  | 15 | Fuse | 1 | Easy-worn |
| 7 | Oil pipe adapter | 1 |  | 16 | Clamper | 1 |  |
| 8 | O Ring | 2 |  | 17 | Cover | 1 |  |
| 9 | Plug | 1 |  | 18 | Power Indicator | 1 |  |