Instruction Manual

ELECTRIC LIFT TABLE

Model: ES30D, ES50D, ES80D

Note: Owner/Operator must read and understand this instruction

manual before using the lift & tilt table.

# ELECTRIC LIFT TABLE

Model ES30D,ES50D,ES80D

## Instruction Manual

READ THIS OPERATION MANUAL COMPLETELY BEFORE USING.THOROUGHLY UNDERSTAND AND FOLLOW ALL SAFETY INSTRUCTIONS.IF THIS IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW COPY.IF THE WARNING/CAUTION DECAL ON THE UNIT IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW COPY.

Note: On this manual, WARNING means the danger which can lead death or serious injury. CAUTION means the danger which can lead slight injury or property damage.

1.  WARNING

1.  DO NOT allow another person to stand in front of or behind lifter when it starts to move.

2.  ALWAYS travel with table in lowered position. Load could fall down.

3.  NEVER sit, stand or ride on platform. SEVERE PERSONAL INJURY could result.

4.  NEVER go under platform. SEVERE PERSONAL  INJURY or DEATH could result.

5.  DO NOT use in area of multilevel floor surface that could create loss control and result in SEVERE INJURY and PROPERTY DAMAGE.

6.  DO NOT use lifter on slope, unlevel or soft surface. Lifter may become uncontrollable. SEVERE PERSONAL INJURY and PROPERTY DAMAGE could result.

7.  KEEP FEET CLEAR of rolling wheels that could result in SEVERE PERSONAL INJURY.

8.  DO NOT load one fork more than the other and DO NOT load tips on forks. SEVERE PERSONAL INJURY and PROPERTY DAMAGE could result.

9.  DO NOT overload lifter .ALWAYS stay within designated capacity and load center rating. SEVERE PERSONAL INJURY and PROPERTY DAMAGE could result.

10. SHEARING HAZARD. NEVER place hands or feet under lowering table. SEVERE PERSONAL INJURY could result.

11. NO FIRE during charging. Read battery operation manual.

12. HIGH VOLTAGE. Disconnect battery socket before opening control panel box.

13. DO NOT remove battery terminal cover. Short-circuit or electric shock could occur.

2. CAUTION

- Hazard or unsafe practice which, if not avoided, may result in MINOR or MODERATE PERSONAL INJURY and PROPERTY DAMAGE.

- READ THE OPERATION MANUAL COMPLETELY BEFORE USING AND THOROUGHLY UNDERSTAND AND FOLLOW ALL SAFETY INSTRUCTIONS.

- This lifter is designed to use with stable uniform load on a solid lever floor. DO NOT use the lifter for any other purpose than its intended use.

- Lifter shall be operated by TRAINED personnel only. OPERATOR shall read “Operation Manual” completely and thoroughly understand the controls and operation of this equipment BEFORE operating the lifter.

- ALWAYS observe lifter and ALWAYS stay at the controls while the lifter is in motion, RELEASE controls and STOP lifter immediately if load on lifter appears to become unstable. NEVER leave the loaded lifter unattended unless the table is in the fully lowered position and the lifter is locked reliably.

- DO NOT slid the load on or off the table. The lift may move allowing the load to fall. SEVERE PERSONAL INJURY and PROPERTY DAMAGE could result.

- DO NOT use lifter with unstable, unbalanced or loosely stacked load. Unbalanced loads may become unstable and fall. SEVERE PERSONAL INJURY and PROPERTY DAMAGE could result.

- ALL  lifter service must be performed by qualified personnel only.

- ALWAYS keep feet, hands and fingers away from casters, load wheels and all moving components. SEVERE INJURY could result.

- ALWAYS perform maintenance and inspections with lifter unloaded.

- Prolonged continous working might cause damage of power pack.

- Stop operation if temperature of hydraulic oil is too high.

The lifter is NOT waterproof and is intended to be used in a dry environment.

3. DAILY INSPECTION

Daily inspection is effective to find the malfunction or faulty on the lifter. Check the lifter on the following points before the operation.

CAUTION

DO NOT use lifter if any malfunction or faulty is found.

- Check scratch, bending or crack on the lifter.

- Check smooth movement of the wheels.

- Check if there is oil leakage.

- Check vertical creep of table.

- Check the function of brake.

- Check if all the bolts and nuts are tightened firmly.

4.NAME OF PARTS

ES30D,ES50D,ES80D

| 1.Handle | 4.Platform |
| --- | --- |
| 2.Switch | 5. Link |
| 3.Brake Pedal | 6.Guide rail |

5.  OPERATING LIFT TABLE

How to use the brake.

CAUTION

Brake lift table when not moving it in order to prevent sudden movement.

The brake is equipped with the swivel caster on the right side.

(1)  Braking the wheel, press the brake pedal.

(2)  Releasing the brake, lift up the brake pedal.

6.  LIFTING UP FORKS

CAUTION

DO NOT overload lifter. Stay within its rated capacity. Prolonged continous working might cause damage of hydraulic power pack. Step operation if temperature of hydraulic oil is too high.

Push the button “UP” and the table lift up.

7.LOWERING TABLE

CAUTION

DO NOT lower table with load too fast and stop suddenly. Impact load could be created and lifter could be damaged.

Push the button DOWN and the table lower.

8.MOVING THE LIFTER

WARNING

DO NOT move lifter on slope or inclined surface, otherwise lifter become uncontrollable and create danger.

- Make the load stable to prevent it to fall.

- Lower the table down.

- Release the brake and move the lifter.

CAUTION

KEEP watching the condition of load. Stop operating lifter if load become unstable.

9.CHARGING THE BATTERY

- Check the quantity of Battery fluid. If it is insufficient, add the battery solution according to battery operation manual.

- Disconnect the battery socket.

- Connect the charging port of battery socket to the battery charger.

10.REGULAR INSPECTION

Perform the regular inspection for the safety operation.

- Check the items expressed in daily inspection (daily).

- Lubricate with grease the guides where roller moves. Also, lubricate the grease nipples. (Every month)

- Lubricate all the pivoting points and axles. (Every 6 months)

- Replace the hydraulic oil for the first time: Accumulated working ten hours’

- Replace the hydraulic oil. (Every 12 months)

11.TROUBLE SHOOTING

| TROUBLE | CAUSE | REPAIR |
| --- | --- | --- |
| Platform do not rise while motor does not run. | 1.Faulty wiring. | 1.Check the wiring referring to the actual wiring diagram. |
|  | 2.Battery socket is disconnected | 2.Connect the battery socket. |
|  | 3.Battery charge is insufficient. | 3.Charge the battery. |
| Platform do not rise while motor runs. | 1.Faulty adjustment of relief valve. | 1.Adjust relief valve again. |
|  | 2.Faulty hydraulic pump. | 2.Replace power pack. |
|  | 3.Shortage of hydraulic oil. | 3.Add oil. |
| Vertical creep of table. | 1.Oil leakage in power pack. | 1.Replace lowering valve. |
|  | 2.Oil leakage form hydraulic circuit. | 2.Check hydraulic circuit and repair. |
| Oil leakage from cylinder. | Faulty sealing. | Replace sealing. |
| Oil leakage from piping or joint. | Insufficient tightening or seal in valid. | Tighten joint again or Replace seal. |
| Oil leakage from air breather. | Excessive quantity of oil. | Reduce oil quantity. |

12. SPECIFICATIONS

| Model | ES30D | ES50D | ES80D |
| --- | --- | --- | --- |
| Capacity (kg) | 300 | 500 | 800 |
| Table (mm) | 520×1010 | 520×1010 | 520×1010 |
| Min. table height (mm) | 495 | 495 | 510 |
| Max. table height (mm) | 1600 | 1618 | 1440 |
| Lifting stroke (mm) | 1105 | 1123 | 930 |
| Motor (KW) | 0.7 | 0.7 | 0.7 |
| Work cycle of hydraulic power pack | 3 times of table moving up-down per 10 min. |
| Approx. numbers of lifting at full charge and with full load.(times) | 45 | 40 | 40 |
| Approx. time required to lift up table.(sec) | 15 | 15 | 18 |
| Wheel (mm, diameter) | 150 | 150 | 150 |
| Handle height (mm) | 1180 | 1180 | 1180 |
| Weight (kg) | 183 | 198 | 215 |

13. HYDRAULIC CIRCUIT/WIRING DIAGRAM/ACTUAL WIRING DIAGRAM

- Exploded View and Part List

#### ES30D

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover φ50×φ58×5 | 1 | 53. | Washer 6 | 12 |
| 2. | Y-ring φ50×φ58×8.2 | 1 | 54. | Hex socket screw M6×16 | 2 |
| 3. | Cylinder cover | 1 | 55. | Battery depressed plate | 1 |
| 4. | O-ring φ56×2.65 | 1 | 56. | Washer 8 | 9 |
| 5. | Piston rod | 1 | 57. | Hex screw M8×20 | 1 |
| 6. | Retaining ring for axle25 | 2 | 58. | Battery | 1 |
| 7. | Bushing | 2 | 59. | Bolt | 2 |
| 8. | Bushing | 1 | 60. | Battery depressed plate | 1 |
| 9. | Pin axle | 1 | 61. | Hydraulic power pack | 1 |
| 10. | Snap ring 50 | 1 | 62. | Electric wire | 1 |
| 11. | Cylinder | 1 | 63. | Up-down Button | 1 |
| 12. | Prevent burst valve | 1 | 64. | Handle | 1 |
| 13. | Spring | 1 | 65. | Nut M4 | 2 |
| 14. | Seal ring 18 | 1 | 66. | Hex screw M6×10 | 4 |
| 15. | Prevent burst joint | 1 | 67. | Covering plate | 1 |
| 16. | Seal ring 14 | 4 | 68. | Nut M8 | 4 |
| 17. | High pressure hose | 1 | 69. | Spring washer8 | 8 |
| 18. | Joint | 2 | 70. | Spacing casing | 2 |
| 19. | Split Pin | 1 | 71. | Spring washer 12 | 2 |
| 20. | Screw M3×20 | 2 | 72. | Hex screw M12×40 | 2 |
| 21. | Washer 3 | 2 | 73. | Hex socket screw M10×25 | 16 |
| 22. | Charging socket | 1 | 74. | Rear wheel | 2 |
| 23. | Spring washer 3 | 2 | 75. | Nut M10 | 16 |
| 24. | Nut M3 | 2 | 76. | Hex socket screw M8×20 | 4 |
| 25. | Covering plate | 1 | 77. | Front wheel | 2 |
| 26. | Washer 4 | 7 | 77A. | Chassis | 1 |
| 27. | Spring washer 4 | 7 | 78. | Table | 1 |
| 28. | Screw M4×10 | 4 | 79. | Roller for table | 2 |
| 29. | Nut | 1 | 80. | Bushing | 2 |
| 30. | Washer | 1 | 81. | Retaining ring for axle20 | 6 |
| 31. | Indicator switch | 1 | 82. | Internal scissors for table | 1 |
| 32. | Screw M3×10 | 2 | 83. | External scissors for table | 1 |
| 33. | Charging capacity Indicator | 1 | 84. | Hex socket screw M8×16 | 5 |
| 34. | Screw M5×20 | 1 | 85. | Pin axle | 3 |
| 35. | Washer 5 | 1 | 86. | Washer | 4 |
| 36. | Fast acting fuse 80A | 1 | 87. | Split pin | 5 |
| 37. | Spring washer 5 | 1 | 88. | Nut M16×1.5 | 5 |
| 38. | Nut M5 | 1 | 89. | Spring pin 8×40 | 2 |
| 39. | Screw M4×16 | 3 | 90. | Lock nut M10×1.5 | 2 |
| 40. | Fast acting fuse 10A | 1 | 91. | Safety rod | 2 |
| 41. | Nut M4 | 1 | 92. | Hex socket screw M10×40 | 2 |
| 42. | Lock Nut M8 | 1 | 93. | Bushing | 10 |
| 43. | Hex socket screw M10×16 | 2 | 94. | External scissors for chassis | 1 |
| 44. | Spring washer 10 | 20 | 95. | Internal scissors for chassis | 1 |
| 45. | Washer 10 | 38 | 97. | Bushing | 2 |
| 46. | Battery case weldment | 1 | 98. | Roller for chassis | 2 |
| 47. | Hex socket screw M5×10 | 4 | 99. | Pin axle | 2 |
| 48. | Joint board | 1 | 100. | Pin axle | 1 |
| 49. | Lifting limit switch | 1 | 101. | Pin axle | 1 |
| 50. | Spring washer 6 | 2 | 102. | Bushing | 2 |
| 51. | Nut M6 | 6 | 103. | Oil cup | 6 |
| 52. | Terminals | 1 |  |  |  |

#### ES50D

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover DH60 | 1 | 54. | Hex socket screw M6×16 | 2 |
| 2. | Y-ring UHS 60A | 1 | 55. | Battery depressed plate | 1 |
| 3. | Cylinder cover | 1 | 56. | Washer 8 | 9 |
| 4. | O-ring φ65×2.65 | 1 | 57. | Hex screw M8×20 | 1 |
| 5. | Piston rod | 1 | 58. | Battery | 1 |
| 6. | Retaining ring for axle25 | 2 | 59. | Bolt | 2 |
| 7. | Bushing | 2 | 60. | Battery depressed plate | 1 |
| 8. | Bushing | 1 | 61. | Hydraulic power pack | 1 |
| 9. | Pin axle | 1 | 62. | Electric wire | 1 |
| 10. | Snap ring 60 | 1 | 63. | Up-down Button | 1 |
| 11. | Cylinder | 1 | 64. | Handle | 1 |
| 12. | Prevent burst valve | 1 | 65. | Nut M4 | 2 |
| 13. | Spring | 1 | 66. | Hex screw M6×10 | 4 |
| 14. | Seal ring 18 | 1 | 67. | Covering plate | 1 |
| 15. | Prevent burst joint | 1 | 68. | Nut M8 | 4 |
| 16. | Seal ring 14 | 4 | 69. | Spring washer8 | 8 |
| 17. | High pressure hose | 1 | 70. | Spacing casing | 2 |
| 18. | Joint | 2 | 71. | Spring washer 12 | 2 |
| 19. | Split Pin | 1 | 72. | Hex screw M12×40 | 2 |
| 20. | Screw M3×20 | 2 | 73. | Hex socket screw M10×25 | 16 |
| 21. | Washer 3 | 2 | 74. | Rear wheel | 2 |
| 22. | Charging socket | 1 | 75. | Nut M10 | 16 |
| 23. | Spring washer 3 | 2 | 76. | Hex socket screw M8×20 | 4 |
| 24. | Nut M3 | 2 | 77. | Front wheel | 2 |
| 25. | Covering plate | 1 | 77A. | Chassis | 1 |
| 26. | Washer 4 | 7 | 78. | Table | 1 |
| 27. | Spring washer 4 | 7 | 79. | Roller for table | 2 |
| 28. | Screw M4×10 | 4 | 80. | Bushing | 2 |
| 29. | Nut | 1 | 81. | Retaining ring for axle20 | 6 |
| 30. | Washer | 1 | 82. | Internal scissors for table | 1 |
| 31. | Indicator switch | 1 | 83. | External scissors for table | 1 |
| 32. | Screw M3×10 | 2 | 84. | Hex socket screw M8×16 | 5 |
| 33. | Charging capacity Indicator | 1 | 85. | Pin axle | 3 |
| 34. | Screw M5×20 | 1 | 86. | Washer | 3 |
| 35. | Washer 5 | 1 | 87. | Split pin | 5 |
| 36. | Fast acting fuse 80A | 1 | 88. | Nut M16×1.5 | 5 |
| 37. | Spring washer 5 | 1 | 89. | Spring pin 8×40 | 2 |
| 38. | Nut M5 | 1 | 90. | Lock nut M10×1.5 | 2 |
| 39. | Screw M4×16 | 3 | 91. | Safety rod | 2 |
| 40. | Fast acting fuse 10A | 1 | 92. | Hex socket screw M10×40 | 2 |
| 41. | Nut M4 | 1 | 93. | Bushing | 8 |
| 42. | Lock Nut M8 | 1 | 94. | External scissors for chassis | 1 |
| 43. | Hex socket screw M10×16 | 2 | 95. | Internal scissors for chassis | 1 |
| 44. | Spring washer 10 | 20 | 97. | Bushing | 2 |
| 45. | Washer 10 | 38 | 98. | Roller for chassis | 2 |
| 46. | Battery case weldment | 1 | 99. | Pin axle | 2 |
| 47. | Hex socket screw M5×10 | 4 | 100. | Bushing | 2 |
| 48. | Joint board | 1 | 101. | Washing | 2 |
| 49. | Lifting limit switch | 1 | 102. | Pin axle | 1 |
| 50. | Spring washer 6 | 2 | 103. | Pin axle | 1 |
| 51. | Nut M6 | 6 | 104. | Bushing | 2 |
| 52. | Terminals | 1 | 105. | Oil cup | 6 |
| 53. | Washer 6 | 12 |  |  |  |

#### ES80D

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal coverφ68×φ60×5 | 1 | 53. | Washer 6 | 12 |
| 2. | Y-ringφ70×φ60×6 | 1 | 54. | Bolt | 2 |
| 3. | Cylinder cover | 1 | 55. | Battery depressed plate | 1 |
| 4. | O-ring φ65×2.65 | 1 | 56. | Hydraulic power pack | 1 |
| 5. | Piston rod | 1 | 57. | Electric wire | 1 |
| 6. | Retaining ring for axle25 | 2 | 58. | Up-down Button | 1 |
| 7. | Bushing | 2 | 59. | Handle | 1 |
| 8. | Bushing | 1 | 60. | Nut M4 | 2 |
| 9. | Pin axle | 1 | 61. | Hex screw M6×10 | 4 |
| 10. | Snap ring 60 | 1 | 62. | Covering plate | 1 |
| 11. | Cylinder | 1 | 63. | Hex socket screw M5×20 | 4 |
| 12. | Prevent burst valve | 1 | 64. | Lifting limit switch | 1 |
| 13. | Spring | 1 | 65. | Spacing casing | 2 |
| 14. | Seal ring 18 | 1 | 66. | Nut M8 | 4 |
| 15. | Prevent burst joint | 1 | 67. | Spring washer8 | 8 |
| 16. | Seal ring 14 | 4 | 68. | Spring washer 12 | 2 |
| 17. | High pressure hose | 1 | 69. | Hex screw M12×40 | 2 |
| 18. | Joint | 2 | 70. | Hex socket screw M10×25 | 16 |
| 19. | Split Pin | 1 | 71. | Rear wheel | 2 |
| 20. | Screw M3×20 | 2 | 72. | Nut M10 | 16 |
| 21. | Washer 3 | 2 | 73. | Hex socket screw M8×20 | 4 |
| 22. | Charging socket | 1 | 74. | Front wheel | 2 |
| 23. | Spring washer 3 | 2 | 75. | Chassis | 1 |
| 24. | Nut M3 | 2 | 76. | Table | 1 |
| 25. | Covering plate | 1 | 77. | Roller for table | 2 |
| 26. | Washer 4 | 7 | 77A. | Bushing | 2 |
| 27. | Spring washer 4 | 7 | 78. | Retaining ring for axle20 | 6 |
| 28. | Screw M4×10 | 4 | 79. | Internal scissors for table | 1 |
| 29. | Nut | 1 | 80. | External scissors for table | 1 |
| 30. | Washer | 1 | 81. | Hex socket screw M8×16 | 5 |
| 31. | Indicator switch | 1 | 82. | Pin axle | 2 |
| 32. | Charging capacity Indicator | 1 | 83. | Washer | 2 |
| 33. | Screw M3×10 | 4 | 84. | Split pin | 6 |
| 34. | Terminals | 1 | 85. | Nut M16×1.5 | 6 |
| 35. | Screw M5×20 | 1 | 86. | Oil cup | 6 |
| 36. | Washer 5 | 1 | 87. | Internal scissors for chassis | 1 |
| 37. | Fast acting fuse 80A | 1 | 88. | Spring pin 8×40 | 2 |
| 38. | Spring washer 5 | 1 | 89. | Lock nut M10×1.5 | 2 |
| 39. | Nut M5 | 1 | 90. | Safety rod | 2 |
| 40. | Screw M4×16 | 3 | 91. | Bushing | 8 |
| 41. | Fast acting fuse 10A | 1 | 92. | Hex socket screw M10×40 | 2 |
| 42. | Nut M4 | 1 | 93. | External scissors for chassis | 1 |
| 43. | Lock Nut M8 | 1 | 94. | Bushing | 2 |
| 44. | Hex socket screw M10×16 | 2 | 95. | Roller for chassis | 2 |
| 45. | Spring washer 10 | 20 | 97. | Washing | 4 |
| 46. | Washer 10 | 38 | 98. | Bushing | 2 |
| 47. | Battery case weldment | 1 | 99. | Pin axle | 2 |
| 48. | Battery depressed plate | 1 | 100. | Pin axle | 1 |
| 49. | Washer 8 | 9 | 101. | Pin axle | 2 |
| 50. | Hex screw M8×20 | 1 | 102. | Pin axle | 1 |
| 51. | Battery | 1 | 103. | Bushing | 2 |
| 52. | Nut M6 | 6 |  |  |  |

# Text boxes

④

①

⑤

②

③

⑥